TALPA
Filesystem Interceptor

OSI Certified Open Source

A Linux kernel module project delivering
high-performance filesystem operation interception

Software Specification

Barry Pearce
barry.pearce@sophos.com
Tvrtko Ursulin
tvrtko.ursulin@sophos.com

Version: 0.9.6

© Copyright 2004-2005 Sophos PLC.

Permission is granted to copy, distribute and/or modify this document under the terms of the GNU Free Documentation License, Version 1.2 or any later version published by the Free Software Foundation; with no Invariant Sections, no Front-Cover Texts, and no Back-Cover Texts.
A copy of the license is included in the section entitled
"GNU Free Documentation License".

Sophos Plc
The Pentagon
Abingdon Science Park
Abingdon
OX14 3YP
UK
Telephone: +44 1235 559933

http://www.sophos.com
barry.pearce@sophos.com

NOTE
Paragraphs marked in orange are still under development!!!

Executive Summary
Description
TALPA is a high-performance filesystem access interception package providing facilities for user-mode daemons/programs to 'vet' filesystem operations before they are executed.
Although primarily designed to meet the needs of high-performance on-access anti-virus scanners, it is not limited to this task and has been designed using generic extensible concepts.
The entire TALPA design considers performance, stability and security as core concepts. It will out-perform other similar modules, has a richer feature set and does not suffer similar issues and design flaws.
Features
- High performance
- Fault tolerant
- High stability
- Dynamically configurable
- Easily extensible
- Caching
- Accurate exclusions without side-effects
- Multiple vetting groups (8)
- Routable vetting (based on filesystems/filesystem types)
- Double-vetting avoidance
- Self-vetting avoidance
- Supports single/multi/hyper-threaded processor systems
- Simple thread-safe API – uses standard open, close, read, write calls, and a single header file.
- Blocking, non-blocking and timed-blocking i/o interface
- Does not require patching or recompiling the operating system kernel
- OSI Certified Open Source licenses
Software Design
Object-oriented approach
- Modular
- Well encapsulated
- Loosely coupled
- Easily extensible
- Has well defined interfaces
- Well documented
Full design available
- UML 2.0
- XMI/1.1 supplied
- Created using Sparx Systems Enterprise Architect v4 (.eap design model file supplied)
Compatible with Rational Rose (XMI/Rose design model supplied)
Operating Systems
Support for
- Linux 2.4 kernels
- Linux 2.6 kernels
- [future] FreeBSD
Tested on
- SuSE 7.1 up to 9.3
- Sun Java Desktop
- Red Hat 7.2 up to 9.0
- Red Hat Enterprise 2, 3 (including RH Advanced Server and Workstation)
- TurboLinux 8 up to 10 (Workstation and Server)
- Mandrake 8.1, 9, 9.1
- Gentoo
- Debian
Client Interfaces
- TALPA Device Driver Vetting Client
- TALPA Process Exclusion Device Driver
Interception Techniques
- Internal syscall-table (Linux 2.4)
- Linux Security Modules (LSM) (Linux 2.6)
- Combined system call interception and VFS table patching (Linux 2.4/2.6)
- [future] Kernel Hooks (a.k.a RAS Hooks and previously a.k.a GKHI) http://oss.software.ibm.com/developerworks/linux
- [future] RSBAC http://www.rsbac.org
Revision History
Version	Date	Name	Description of changes
0.1	2004-04-28	Barry Pearce	Initial creation. Sections 3-6 outstanding.
0.2	2004-04-29	Barry Pearce	Changes following initial peer-review comments. Licensing section modified.
0.3	2004-05-27	Barry Pearce	Minor changes to Licensing of Kernel Modules. Continued development (incl) - layered architecture & multiple modules added. - cache design by Peter Higginson added. / Initial iteration objectives documented (SyscallIntercept, StandardInterceptProcessor and Configurator).
0.3.1	2004-05-27	Barry Pearce	Added in details of filesystem service layer packages.
0.3.2	2004-06-14	Barry Pearce	Diagrams updated to reflect latest.
0.3.3	2004-06-16	Barry Pearce	Minor amendments following partial-review by Tom Thacker.
0.3.4	2004-06-21	Barry Pearce	Diagrams brought up to date with regard to the model. Minor corrections & continued development. Added Personality package and talpa-linux kernel module information.
0.4	2004-07-13	Barry Pearce	Added design of Inclusion processor, Degraded Mode processor, thread exclusion processor, and the filesystem object exclusion processor. / Added full configuration details.
0.5	2004-07-21	Barry Pearce	Completed vetting client protocol and device driver interface. / Added OperationExclusionProcessor intercept filter (eval filter). / Added DenialSyslog intercept filter (deny filter)
0.6	2004-07-28	Barry Pearce	Added ProcessAndThread and LinuxProcessAndThreadImpl packages. / Added VettingController and IvettingServer description. / Added Device Driver Vetting Client description.
0.7	2004-11-04	Tvrtko A. Ursulin	Configurable parameters and protocol specification updated according to the latest changes.
0.8	2004-11-10	Tvrtko A. Ursulin	Added symlink and link-unlink known limitations.
0.9	2004-11-11	Tvrtko A. Ursulin	Documented the I/O API packets.
0.9.1	2004-11-12	Tvrtko A. Ursulin	Added documentation on configurable interceptors.
0.9.2	2004-12-09	Tvrtko A. Ursulin	Documented stream unlink and truncate packets.
0.9.3	2005-02-22	Tvrtko A. Ursulin	Documented new VettingController and ThreadExclusion module parameters.
0.9.4	2005-04-20	Tvrtko A. Ursulin	ThreadExclusion renamed to ProcessExclusion. / Support modules added to component list. / ProcessExclusionDeviceDriver changes. / Version 3 protocol changes.
0.9.5	2005-06-10	Tvrtko. A. Ursulin	New VettingController confguration option added. (X smart scheduler workaround)
0.9.6	2005-06-21	Tvrtko A. Ursulin	Bringing the document up-to-date, changes all over the place.

Last Modified:	Tvrtko Ursulin	2005-06-21	17:16:16
Last Printed:	Tvrtko Ursulin	2004-11-11	12:12:16

Outstanding Items
- Cache
- Dynamic Behaviour diagrams
Contents

# Introduction
What's in a name?
So what's all this 'TALPA' stuff then?
Well its tenuous at best but I'll try to explain. The word TALPA comes from Genus TALPA which is a European mole (Insectivora; Talpidae; Genus TALPA).
But why a mole?
You mean other than the fact they are quite cute?! Well the word mole has two connotations. Firstly in terms of spying a mole avoids being noticed and passes information onto interested parties. Secondly, moles burrow – and that's what we are doing here...burrowing around digging up all sorts of bits of information which come out above ground (kernel J).
I did say it was tenuous!
But honestly apart from the above, TALPA is a unique name within the open source community, and from searches appears to be unused, indeed not even partially referenced by another software project - which is a tall order these days!
Purpose
The document describes the design of the TALPA kernel module and captures the design decisions and trade-off's that are made. This document also is the primary reference for specification of the interfaces.
Scope
This document is restricted to design specification and will attempt to avoid implementation details, except where these are (due to the nature of the project) critical to the design. Implementation details will be discussed in the TALPA Implementation Description document.
It is intended to be read by managers and software engineers involved in design, implementation or integration.
Documentation
All documentation has been produced using OpenOffice, and published as Adobe PDF.
Models
UML 2.0 is used throughout to describe the design. If you are unfamiliar with UML please refer to [UMLU] and [UMLR].
Where appropriate UML OCL (Object Constraint Language) is used to enhance the UML specification. If you are unfamiliar with OCL please refer to [WARMER].
Design patterns have been used as part of this design. If you are unfamiliar with design patterns please refer to [GAMMA].
The models referenced here were created using Sparx Systems Enterprise Architect v4.0 Corporate Edition, and are published as .EAP as well as XMI/1.1 and XMI/Rose for maximum portability.
References
Version	Date	Name	Source
0.1	2004-04-28	Barry Pearce	TALPA Implementation Document / TALPA-ImplementationDescription.sxw
n/a	2004-04-28	Barry Pearce	TALPA Software Specification Model

# Overview
Introduction
TALPA is a high performance filesystem access interception module providing facilities for user-mode daemons/programs to 'vet' filesystem operations before they are executed. Although primarily designed to meet the needs of high-performance on-access anti-virus scanners, it is not limited to this task. The entire TALPA design considers performance, stability, security, genericity and extensibility as core concepts. It will out-perform other similar modules, has a richer feature set, and does not have the associated issues and design flaws.
The diagram below shows a high-level component diagram showing the key components in TALPA.
Once the TALPA kernel modules have been loaded external user-mode daemons may use a device driver interface (via the DeviceDriverVettingClient) to register as an interested party with the VettingController.

When a process or thread executes one of the intercepted operations the Interceptor kicks in and directs the attempt to an Intercept Processor. The InterceptProcessor uses a set of InterceptFilters to decide whether to allow or deny the operation. One of these filters is the VettingController. The VettingController will pass vetting requests to previously registered interested parties, and wait for a response. The response is then passed back to the InterceptProcessor. Once all the necessary filters have been called the decision is returned to the Interceptor, which in turn will allow or deny the operation.
These components and their responsibilities are described in more detail below, and will be described in full in later sections of this document.
A number of design decisions were taken regarding the architecture as it is now. And it is important to understand why these decisions were made and their impact on the design.
The biggest factor in the design of TALPA was whether or not open file descriptors should be passed to userspace as a performance optimisation. The passing of open file descriptors across to another process is only supported via unix domain sockets. However, sockets produce a number management issues, especially regarding failure scenarios. Under test conditions a standard open and close combination on a file took 4μs. It was therefore decided that the 4-10μs delay caused by an additional open() would be saved through other efficiencies through good quality design of the system itself.
Because the open file descriptor is not passed to userspace it was decided that the communications with userspace should be provided using interchangeable components, thus allowing the VettingController to concentrate on mediation.
Other interception packages suffer performance issues because of translation of binary data to another form. To avoid performance penalties it was decided that the interface between userspace and the kernel should be based on binary data. It was thus decided that we would like the features of the device file and the unix message queue combined.
We shall now take a brief tour of the major components.
Interceptor
The Interceptor is responsible for either hooking the operating system 'syscall' table or interfacing with other hook mechanisms (such as LSM, RSBAC or Kernel Hooks). When an interception occurs an InterceptProcessor is called to examine the attempted operation. The InterceptProcessor will respond indicating whether or not to allow the operation to proceed. If the interception mechanism was 'syscall' table hooking and the operation is allowed, control is passed onto the original operating system call to service the request. However, if denied an error is returned to the client. All other intercept mechanisms require an allow/deny response from the Interceptor and will take the appropriate action themselves. In this case the InterceptProcessor's response is merely passed on.
The Interceptor may be enabled or disabled, thus providing an overall enable/disable switch for the entire interception package.
Intercept Processor
This is a lightweight component, responsible for controlling examination and evaluation of the attempted filesystem operation. The InterceptProcessor maintains three collections of InterceptFilters; evaluation-actions, allow-actions and deny-actions collections. When an intercept is given to the InterceptProcessor for examination each filter defined in the evaluation-actions collection is called in turn. Each filter may then either allow, deny the operation or identify itself as 'indifferent' (next) or identify a timeout or error occurred and the filter did not complete. After the evaluation-actions collection has been processed a decision to allow or deny the operation will have been made. If an error occurred the filesystem operation is refused with the error provided as the reason, otherwise, each filter in either the allow-actions or deny-actions collections will be processed before the result of the examination is returned.
Intercept Filters
InterceptFilters are the decision making core of TALPA, and are based on the Strategy[GAMMA] design pattern. When used for evaluation each filter may return ALLOW, DENY, NEXT, TIMEOUT, or ERROR. When used as allow or deny actions each filter does not return a result.
A number of filters will be developed providing sophisticated, high-performance evaluation of filesystem operation attempts. Each filter will focus on a single aspect of the decision making. We will examine each of the filters in turn.
Degraded Mode Processor (evaluation-action)
This is a stability filter. The InterceptProcessor provides information about the number of consecutive time-outs, based on the number of attempted operations that had one of the filters return TIMEOUT. When the number of time-outs is below a trigger level this processor merely indicates that it is indifferent (NEXT) to the request. Should the number of time-outs pass a trigger level then 'Degraded Mode' will be enabled. In this mode all requests made by a 'root' process/thread will be forcibly allowed, indicating that no further filters should be called. All other 'user' processes will still have to pass through the other filters. This means that 'root' bypasses any subsequent filters. Because all NFS daemons typically run as root, this produces a security issue, and therefore may be switched off. However this mode does have the advantage of keeping the operating system alive so that the 'root' user may resolve the problem or shutdown/reboot the system.
Process Exclusion Processor (evaluation-action)
With all vetting systems there is a danger of self-vetting - attempting to vet the vetter's actions. This can lead to a infinite -loop and hang the system – obviously undesirable. Whilst this would be (and is) checked by the vetting controller it is possible that the excluded thread did not work alone and would need to pass the vetting request onto another thread. This thread would then need excluding as well for the same reasons.
In the anti-virus world it is imperative that an on-demand scanner or infection removal tool is not restricted by an on-access scanner; double-vetting should therefore be avoided. For instance, we have a threat (virus/worm/trojan) infected file on the disk, and an on-demand scanner is asked to scan the file. The on-demand scanner attempts to open the file, but access will be refused because an on-access scanner detected the threat (double-vetting has been attempted). Thus the on-demand scanner will not report the threat – nor would disinfection be possible! Again a less than desirable situation.
Therefore TALPA includes mechanisms for processes other than vetting clients to be excluded from the vetting process. The mechanism provided is based on an internal list of excluded processes. To obtain an exclusion a thread must open up the process exclusion device file and use an 'ioctl' to control setting/un-setting of the exclusion.
Operation Exclusion Processor (evaluation-action)
This filter provides filtering based on the operation itself. For instance opening a file with truncation may not require external vetting, and therefore will be excluded from subsequent processing. The following file operation exclusions will be supported
- Open for write only
- Open for write or read-write with truncation
- Open for append only
- Close when opened read-only (already vetted!)
Filesystem Exclusion Processor (evaluation-action)
This filter screens out attempted filesystem operations on objects that do not require subsequent processing such as that provided by the VettingController. Exclusions may be provided based on
- File system type
- Simple pathname matching (directories/mount points/files)
Typically the following special file types would be excluded from vetting by a virus scanner
- Directories
- Symbolic links
- Named pipes
- Named (bound) sockets
- Character devices
- Block devices
When a filesystem operation attempt is evaluated for pathname exclusions by this filter, the absolute pathname will be used. Matching is based on simple left-right comparisons, with the following provisions:
- Directory/sub-tree exclusions must be specified with a trailing pathname separator. These will match a directory path regardless of whether or not the pathname being checked includes a trailing pathname separator. The exclusion itself must be fully matched, however the pathname checked may partially match allowing entire sub-trees to be excluded.
- File exclusions do not have a trailing pathname separator and both exclusion and the pathname must be matched in full.
Cache
The cache mechanism is used to enhance performance. Typically a subsequent filter (such as the VettingController described below) will perform a time-consuming activity (such as virus scanning) in order to make its decision. The cache aims to speed up by processing by storing responses to previous requests. If no changes have been made the cached result will be used avoiding the need to execute further filters. The cache will be configurable, so that it may be turned on/off globally (as described above), and what is or isn't cached may be specified using the generic configuration mechanisms described below.
Cache Check Processor (evaluation-action)
Merely checks the cache for an entry. If an entry is found the filter responds indicating the operation attempt should be forcibly allowed, otherwise the response should indicate indifference.
Cache Update Processor (allow-action and deny-action)
Updates the cache in two circumstances. Firstly a new result is available and should be entered into the cache or secondly an operation has occurred which affects the cache - typically this will involve removal of the cache entry.
Vetting Controller (evaluation-action)
In practical terms the Vetting Controller provides a mechanism for passing vetting requests onto 3rd parties and allows them to provide a decision the attempted filesystem operation.
The vetting controller thus provides a message routing system using client-server based principles, providing blocking, non-blocking and timed-blocking message interfaces.
Typically, an number of user-mode daemons will register with the vetting controller through the device driver interface. Once registered, daemons may indicate their readiness to accept vetting requests. When an attempted filesystem operation is passed into this filter, it is passed onto one of the external daemons for vetting. The typical response would be ALLOW or DENY, however, it is possible that the external daemon fails and does not respond, or responds after an unacceptable length of time. In either case the VettingController will return a TIMEOUT response.
Syslog (evaluation-action)
The filter is used mainly for debugging purposes. Every time this filter is invoked it records the information about the intercept to the system log.
Denial Syslog (deny-action)
This filter is similar to the Syslog filter, however it is designed to output information specifically related to a denial of access. Additional information will be logged describing why an operation was refused.
Device Drivers
Two device driver interfaces will be provided by TALPA.
The DeviceDriverVettingClient component provides an externalised interface to the VettingController. Based on the Adapter[GAMMA] design pattern this interface provides a standard I/O system API interface, that may be used to obtain and respond to vetting requests.
The ProcessExclusionDeviceDriver component provides an externalised interface to the ProcessExlusionProcessor. This interface provides a standard I/O system API interface that may be used to set and unset process exclusions as described above.
Dynamic Configuration
Every component will support a configuration interface providing support for procfs/sysctl. This allows each component to have its own configuration parameters without a centralised configuration mechanism.
This means all components may be dynamically configured using the procfs/sysctl interface, providing a method of enabling/disabling interception, or filters on-the-fly.
Kernel Modules
All the functionality and components above are packaged in a number of kernel module object files, providing a flexible extensible change-tolerant system.
# Design specification
Introduction
This section describes in detail the TALPA architecture and design. It attempts to capture and explain some of the reasoning behind the major design decisions.
The approach and philosophy used to drive the design and development are critical for the quality of the software. It is therefore worth describing some of the main driving concepts behind the design, even though much of this is just good OO design principles.
OO design sympathetic to the target implementation
It was decided that an object-oriented approach should be used for the TALPA design, even though the implementation language would be C. Because of this inheritance should be severely restricted, as true polymorphism would be costly to implement. Therefore much of the design is focused on specifying a number of single-level abstract interfaces and providing n implementations that support those interfaces, rather than n-level inheritance hierarchies using either interface or implementation inheritance.
Based on highly-cohesive loosely-coupled components
The design focuses on the use of encapsulation and modularisation through the wide use of abstract interfaces and minimising of dependencies. At no point would direct or indirect cyclic dependencies be allowed. The result should provide a high-stability software system that encourages highly-concurrent, parallel development of the components.
Resilience to change and minimising propagation of change
Through the careful use of encapsulation and abstract interfaces propagation of change should be minimised such that changes to the implementation of one component should not propagate through to any code outside of that component. Additionally the design should limit propagation of interface changes to direct dependants only. A change to an interface should not therefore propagate to another interface resulting in a domino effect.
It is this philosophy coupled with the highly-cohesive loosely-coupled component concept that helps ensure the ultimate stability of the code base and the design.
Extensible
The architecture should not resist change, but welcome extensibility whilst preserving the highest degree of resilience and stability. This is again the result of a focus upon encapsulation and widespread and diligent use of abstract interfaces.
Performance
TALPA should be considered and approached in a manner more in keeping with an embedded real-time system. In particular memory, CPU usage, speed/throughput and concurrency must be given due consideration throughout the design and implementation.
This document will not duplicate the detailed information in the model. It will provide a reasonably detailed look at the model, but the intention of this document is to promote understanding.
Layered architecture[1]
[1] If you are unfamiliar with layered architectures please see [FOWLER] and [JACOBSON].
Tiered architectures provide better stability of code/design and encourage greater re-use through the use of separation (loose coupling) and well-defined interfaces.
TALPA will use a three tier software architecture. The architecture is based on a four tier concept, but as there is little sensible use for a domain layer it has been removed.
The diagram below shows the division of major component groups into the architectural layers.

Although this document will not describe the principles of tiered architectures in general it is worth explaining the basic 'features' of the architectural layers shown in the diagram above.
Presentation layer
The presentation layer has traditionally referred to UI. However, with TALPA it is sensible to consider the external interface components as presenting an interface for use externally. It is effectively through these interfaces that TALPA is used. The presentation layer should be considered as completely replaceable and that replacement of the presentation layer components would in no way affect the application logic. With TALPA this is true, especially with regard to the vetting clients. Here only one interface is currently presented; that of a device driver. However, this could equally be replaced with a socket or UNIX message queue interface without changes propagating to any other layer.
Application layer
This is the heart of the system and typically encapsulates the logic that defines our system. In TALPA this is where the core functionality resides. This should be the layer that contains the most portable code.
Services layer
The services layer typically encapsulates databases, operating system services and features such as threading. With TALPA we will rely only on o/s services; more specifically the kernel API.
One of the underlying principles of tiered architectures is that a package or component at one level may only have dependencies on packages/components in the same or lower layers. Failure to adhere to this results in spider-web systems which are difficult to maintain.
Due to the nature of kernel integration it is not possible to have a layered system where o/s dependencies are encapsulated in a single architectural layer. Indeed, in a kernel module almost all external interfaces will be o/s dependent, the core for the most part will can be isolated but naturally will have to rely on o/s dependent services.
It should therefore be noted that operating system dependency is not shown in, and should not be inferred from the diagram. Due to the nature of the system, all presentation layer components expose external interfaces, and are highly operating system dependent. Therefore from an architecture perspective we end up with a sandwich, with only the application layer remaining operating system independent.
### Component grouping
TALPA is structured into six component groups. Each group in turn consists of one or more component packages. The component groups are aligned with the layered architecture defined above. The grouping is based on creating cohesive packages, where high-level dependencies are minimised. The component groups are described below, along with the main objects that they contain.
Intercept components
This group focuses on the Interceptor based objects. Each component package within this group provides support for a single interception mechanism. These components are completely interchangeable, however, only one instance of any of the component packages would be used at any point in time.
Filter Interface components
This group provides external interfaces to InterceptFilters that may be used for additional command and control. For products that are not to be shipped under GPL this must be an interface based on standard system calls (sockets, i/o subsystem etc.). These components are interchangeable, and any number of instances of these component packages may concurrently exist. This allows both a device-driver interface and a socket interface to be supported concurrently.
Core components
This group contains the main functionality of TALPA; the intercept processor, filters and configuration objects.
Service components
This group contains the configuration classes and classes that are used to encapsulate operating system specifics, providing cross-platform support.
Application-Control components
Every system requires application-level system-specific entry and exit code to bootstrap, create and control the objects which form the system itself. For TALPA this application code is embodied in the 'application-control kernel-module' components, which support a Linux Kernel Module interface.
The kernel module components are described in detail later.
### Physical component packaging
The component packages and groups described above will be packaged into the following kernel-modules.
Support components
talpa_syscallhook	Support for Linux syscall table hooking.
talpa_capability	Linux LSM module which provides default capabilities and exports an interface for talpa_lsm.
stacker	Generic Linux LSM stacking module.
talpa_pedconnector	Used to connect talpa_pedevice with talpa_core and talpa_linux.

Intercept components
talpa_syscall	Support for Linux 2.4 syscall interception
talpa_vfshook	Support for Linux 2.4/2.6 filesystem patching/interception at VFS layer.
talpa_lsm	Support for Linux 2.6 LSM and talpa_capability interception.
talpa-rsbac	Support for RSBAC
talpa-khooks	Support for Kernel Hooks (RAS/GKHI)

Filter Interface components
talpa_pedevice	Support for a device-driver interface to the ProcessExclusionProcessor.
talpa_vcdevice	Support for a device-driver interface to the VettingController.

Core and Service components
talpa_core	Contains the standard intercept processor, intercept filters, and configuration code.
talpa_linux	Contains filesystem, and user personality service-layer operating system dependent code.

As described in the previous section each module will be driven by a kernel module component object which supplies entry/exit code and external symbol information (interfaces) for use by other kernel module components. At no point should one kernel module attempt to directly access symbols for non-interface objects in another kernel module. All objects and interfaces should be obtained via the appropriate kernel module component's exported interface.

NOTE: It may make sense to move the configuration to the talpa-linux module due to its interaction with sysctl and procfs....however, this decision is probably best deferred until the differences between different operating systems procfs can be established.
Design Overview
### Introduction
As described above the TALPA architecture makes extensive use of abstract interfaces. To this end the entire system may be described using these interfaces. To ensure clean separation and maximise loose-coupling all the abstract interfaces are placed in 'abstract packages'. These abstract packages only ever contain 100% pure abstract interfaces. Obviously there needs to be some implementation behind these interfaces to make the system actually work. The implementation classes that realise and support the abstract interfaces are packaged into a set of 'concrete packages'.
It is a fundamental principle that concrete classes may only be shared intra-package. All inter-package dependencies and relationships must be on abstract interfaces from 'abstract packages' only. One exception to this rule is allowed; the application-control components out of necessity must create the concrete objects. The three application-control packages are therefore allowed to have concrete package dependencies.
The diagram below shows the main class packages within TALPA, the diagram covers the three architecture layers but does not cover the application-control classes (these are described below).

Cyclic dependencies are non-existent and in line with fundamental principles the implementation classes depend only on abstract interfaces. This overview is useful as a general picture of the 'object' landscape. Subsequent sub-sections of this document will examine each of the component groups.

The application-control component code is shown in the diagram below.

It should be noted from the diagrams that in accordance with the design principles implementation packages (concrete packages) do not rely upon each other, except for the module packages that contain the application-control classes.
As a guiding principle for security, it is assumed that if root access is required to perform subverting actions then the operating system is already compromised, so there is no point in elaborate security mechanisms to protect against the complete loss of the system control.
### Stubbing
Because of the widespread use of abstract interfaces it is easy to create stub code if necessary to simulate functionality which is yet to be developed, or as an aid to isolating problems. The main centres of object creating are the application-control classes. Thus most stubbing can be resolved by instantiating different objects.
It would be relatively simple to extend the application-control code to provide dynamically switchable stub objects, thus allowing a simple configuration change via procfs to switch in or out the stub object. Such dynamic switching may be used to great effect when isolating code for debugging or 'triggered' debugging.
### Dynamic debugging
In the same way stub object may be instantiated, so may debug objects. The preferred method of inserted code-level debugging would be to create proxy[GAMMA] classes. These proxies may then be used either instead of the actual implementation (in a manner similar to a stub – a debugging stub if you like), or they may be used transparently, forwarding requests onto the original objects.
INTERCEPT COMPONENTS
### Interceptor

HOW TO USE
Instantiate a concrete interceptor, call addInterceptProcessor() with the InterceptProcessor that is to receive the intercepted filesystem operation details, and then call enable(). When enable() is invoked the appropriate mechanism for hooking will be initialised and the InterceptProcessor will start receiving intercepts.
To disable interception the disable() method should be invoked. It should be noted that the Interceptor is not responsible for the InterceptProcessor. It is the responsibility of the calling object to ensure that the InterceptProcessor exists as long as the Interceptor has a reference to it. Additionally the Interceptor will never destroy an InterceptProcessor.
#### Syscall-table Interceptor

The syscall-table interceptor provides support for Linux 2.4 kernels.
Under Linux system calls are made between user-mode and kernel-mode by the use of interrupt, and an integer that identifies the required kernel function that should be called. Once in the kernel a lookup is performed using the integer identifier. The target of the lookup is a table of function pointers - the syscall-table. The function pointed to is then called.
The syscall-table interceptor uses the talpa_syscallhook module to register it's hooks to be called by talpa_syscallhook as a system call authorisation mechanism.
The diagram above clearly shows the TALPA interceptor functions providing authorisation hooks: open(), close(), execve(), mount(), umount() and uselib().
When an intercept occurs the IFilesystemFactory abstract factory is used to create an operating system independent objects that encapsulate the details of the operation. For a close operation the original function is invoked at this point. Then one of the examine methods of the InterceptProcessor then invoked as appropriate for the operation. For all operations except close, if the examine method returns ALLOW then the original function is invoked. Otherwise the operation is rejected.
#### LSM Interceptor
Linux security Modules were made available from Linux 2.5.29, and given major release as the syscall-table hooking replacement in Linux 2.6 kernel.

In the Linux 2.6 kernel the syscall-table is dynamically allocated, with at least some intention of halting the syscall-table hooking practice as used above. In order to provide security systems with a means to 'vet' operations new functionality was required. This functionality was presented in the form of Linux Security Modules (LSM). LSM is a framework programming interface that is based on registering a module that may later receive operations for security vetting.
The basic way it works is that a module registers as an LSM and provides a set of functions that describe a security policy. These functions are called by the kernel as appropriate to evaluate the security policy, and either allow or deny access. One further complication is that only one module is allowed to register. Any subsequent modules must register with the first module, and any chaining characteristics are undefined.
TALPA will provide an LSM module. Operation is similar to, but significantly simpler than the syscall-table interceptor.
When an intercept occurs the IFilesystemFactory abstract factory is used to create an operating system independent objects that encapsulate the details of the operation. Then one of the examine methods of the InterceptProcessor then invoked as appropriate for the operation. If the examine method returns ALLOW then the operating system allows the access, otherwise the operation is rejected.
#### VFSHook Interceptor

This interceptor tries to overcome several problems which are present on 2.6 kernels if trying to use LSM interceptor. Since it does not depend on LSM support being compiled into the kernel, nor does it depend on another LSM module being already loaded, it can be used in almost every situation. (it also works on 2.4 kernels) It depends on talpa_syscallhook module beign lodaded with hook_mask=mu because it uses its services to install it's mount/umount hook. Therefore if talpa_syscallhook is unable to hook the system call table it will fail to work. As of this writing (17.06.2005), it is not known for it to fail but it is still possible that the mechanism it uses to find hidden syscall table will not work on future 2.6 kernels.
What it does is, it finds a regular file on each mounted filesystem and patches struct file_operations (or temporarily struct inode_operations) so that our functions are called instead of filesystem's ones. It also intercepts mount/umount operations and in that way catches addition of a new filesystem.
When an intercept occurs the IFilesystemFactory abstract factory is used to create an operating system independent objects that encapsulate the details of the operation. Then one of the examine methods of the InterceptProcessor then invoked as appropriate for the operation. If the examine method returns ALLOW then the operating system allows the access, otherwise the operation is rejected.
CORE COMPONENTS
### Intercept Processor
Intercept Processors may be used to evaluate an attempted filesystem operation.

HOW TO USE
Instantiate a concrete processor. Add the required evaluation, allow and deny filters. The processor is now ready for use The examine() method is used to request the processor to examine a file or filesystem based operation. To call these methods, a IFileInfo or IFlesystemInfo must first be instantiated with the relevant details, and passed into examine(). The examine() method will return 0 if the operation should be allowed, or and error code (NZ) if it should be denied.

#### StandardInterceptProcessor
The StandardInterceptProcessor provides the default intercept processor functionality for TALPA. It is based on an execution of the Strategy[GAMMA] design pattern, where a set of algorithms are encapsulated and may be executed without reference to individual algorithms.

Configuration is provided through realisation of the IConfigurable interface.
Once instantiated the StandardInterceptProcessor object may be passed into an IConfigurator object to allow dynamic configuration. The processor is then made ready for use by adding evaluation intercept filters. Allow and deny filters may be added as required.
To request evaluation, a client calls one of the examine() methods. When an examine() method is called a new EvaluationReportImpl object is instantiated, and is passed the current value of mNumConsecqutiveTimeouts. The EvaluationReportImpl sets the initial mRecommendedAction to EInterceptAction::Next.
The StandardInterceptProcessor will now call each intercept filters defined in mEvaluationActions in turn, passing in the EvaluationReportImpl. The filter evaluates the associated operation details and alters the recommended action in the evaluation report. If the action is still EInterceptAction::Next or EInterceptAction::Timeout then processing of filters continues, otherwise the remaining evaluation filters will be skipped.
Once processing of the evaluation filters stops a decision has been reached; EinterceptAction::Allow and EinterceptAction::Next will produce an 'allow' response. EinterceptAction::Deny, EinterceptAction::Error or EInterceptAction::Timeout will produce a 'deny' response. If the recommended action was EInterceptAction::Timeout then the mNumConsecqutiveTimeouts is increased by one. Any other action will result in this value being reset. With the decision made the intercept filters in either the mAllowActions or mDenyActions collections are executed according to which response is to be made.
Finally, the method returns true if an 'allow' response is required, otherwise it will return false.
The EvaluationReportImpl is relatively straightforward. CustomData support is based on the use of the EvaluationData objects. When the EvaluationReportImpl is destroyed so must all of the CustomData. The EvaluationData objects will be stored in a double-linked list.
### Intercept Filters
As described above intercept filters are the major part of the embodiment of the Strategy[GAMMA] design pattern. Their role is respond to requests to evaluate a filesystem operation according to a set of criteria.

HOW TO USE
IInterceptFilter
These objects are extremely simple to use, although they may encapsulate significantly complicated algorithms. They may be used by simply instantiating them and then invoking an examine() method, passing in both a report object and the operation details.
Each filter may also be enabled/disabled independently of the InterceptProcessor that they are associated with. By default a filter is enabled, but this may be controlled using the enable() and disable() methods.
IEvaluationReport
The report object is used to store the response to the request, and the CustomData methods allow passing of data between filters. The CustomData storage mechanism provides a de-coupling of filters – thereby avoiding one filter from depending directly on another at code level. It is the responsibility of each individual implementation to supply some method for storing the custom data that may be used to pass information between filters.
To obtain the response to a particular request then the getRecommendedAction() method of the report object should be invoked.
#### Degraded Mode Processor
The degraded mode processor will sacrifice interception in order to ensure stability. Degraded mode allows root to continue to work (by bypassing vetting) when other users may not; thus allowing the operating system to be shut down gracefully. If the real uid of the calling process is 0 and the consecutive number of timeouts as specified by the calling InterceptProcessor (in the evaluation report) is equal to, or greater than the threshold value then the operation is immediately allowed bypassing all subsequent filters.

The degraded mode processor also provides monitoring via the 'active' read-only configuration item. See the Interface specification for further details.
#### Process Exclusion Processor
Whilst this functionality could have been placed in the vetting controller it is better that it is external. This provides optionality, code stability, and independent configuration and replacement, compared to embedding the component in the VettingController.

The basic concept behind the process exclusion processor is to maintain a list of excluded processes. When the filter is invoked through the examine methods the list is checked to see if the thread invoking the intercepted operation is on the list. If it is then the filter immediately allows the operation to be performed, bypassing subsequent evaluation filters.
This behaviour allows on-demand and on-access virus scanners to use TALPA, without the performance of interaction issues.
The list is based upon an operating system independent concept of process and process id. To be excluded the process must first register (registerProcess()), and may then toggle the exclusion as required (using active() and idle()). When complete the process should deregister (deregisterProcess()). The Process Exclusion Device Driver provides an interface for userspace threads to perform registration and exclusion toggling. Further details may be found by examining the appropriate section below.
#### Filesystem Inclusion Processor
The filesystem inclusion processor provides screening of operations, such that operations on a defined directory hierarchy are subject to subsequent filters, whereas operations outside the directory hierarchy specified are not. The inclusion path is set via the 'include-path' configuration item. It is always considered to be a directory, and as such will always have a terminating slash.
When an operation is screened the target pathname is checked against the inclusion-path. If the target pathname includes the include-path then the operation will be subject to vetting, and the filter returns EIA_Next otherwise it returns EIA_Allow. If the target-pathname is one character shorter than include-path, matches that extent and is a directory it will also be subject to vetting.

This filter for performance reasons, is disabled by default. This effectively defaults the path to '/' and will result in all operations being vetted fully. If the filter is enabled and the 'include-path' is set to '/' the filter will also be disabled, again for performance reasons as this avoids a string comparison.
#### Filesystem Object Exclusion Processor
The Filesystem Object Exclusion Processor provides simple exclusion processing. The exclusions are configured using the procfs/sysctl interface – these are described in the interface specification section. Again the filter may be enabled or disabled through the configuration interface.
When an examine method is invoked a number of checks are performed, these differ for files and filesystems.
Files
The file is first compared against the special files mask. This mask provides a simple bit-wise comparison which provides exclusions for directories, symbolic links, pipes (fifos), sockets, block devices, and character devices. The filesystem that the file resides on is then compared with each filesystem exclusion defined in the list mExcludedFsTypes. Finally the filename is checked against the list of excluded paths; mExcludedPaths). If at any time the file should be excluded, the recommended action is set to EIA_Allow and all subsequent filters will be bypassed.
Filesystems
This is typically called on mount or umount. The filesystem type is then compared with each filesystem exclusion defined in the list mExcludedFsTypes. If the filesystem type appears in the list then the recommended action will be set to EIA_Allow and all subsequent filters will be bypassed.

#### Operation Exclusion Processor
The Operation Exclusion Processor provides screening of individual types of operations. The filter will return an ALLOW for the following operations:
- Open for write only
- Open for write or read-write with truncation
- Open with exclusive-create
- Open for append only
- Close when opened read-only (already vetted!)
None of these operations allow the client process to read existing data in the file and therefore continuing the evaluation through the VettingController is probably inappropriate. The OperationExclusionProcessor has one configuration element; it may be enabled or disabled via procfs or sysctl. By default the OperationExclusionProcessor is enabled.
This filter has no affect on filesystem operations and returns without action.

#### Syslog
The Syslog Filter is not a production intercept filter. It may be used to log every intercepted operation into the system log (typically /var/log/messages). The Syslog Filter has one configuration element; it may be enabled or disabled via procfs or sysctl. By default the Syslog Filter is enabled, however, unless configured using --enable-syslog in the Syslog Filter is not available in the production environment.

#### Denial Syslog
The DenialSyslog filter may be used to log every denied operation into the system log (typically /var/log/messages). The DenialSyslog filter has one configuration element; it may be enabled or disabled via procfs or sysctl. By default the DenialSyslog filter is enabled.

#### Cache
#### Requirements
Caching of virus scan results is a requirement for Peanut. It must be possible to exclude certain file systems from caching – for example smb shares.
We need to produce a good cache scheme because the cache overheads are added to all checks. For files not in the cache it takes longer to do the complete virus check than it would if there was no caching. Since many files are read once only the cache check must be very low overhead. (Gain = hit rate - cache time/virus time, so if the hit rate is less than the time ratio you lose.)
#### Mounted Filesystems
Because remote file systems can be modified without local knowledge, it is assumed that there is a “cache inclusion list” that the user sets up. It would make sense to have an inclusion/exclusion list based on filesystem types.
The user needs to have some control over caching because some types of disk array might be shared by several systems and whether a particular area is set up as private to one system or not is down to the user’s configuration.
#### Cache States
The cases of excluded and unsafe (e.g. permitted in degraded mode) might be handled by not having a cache entry. A check-in-progress state may be needed if we decide to optimise the case of near simultaneous access to the same file.
We can take the view that denies are very rare or treatable as an error case and  only save permits in the cache. This requires there to be an unused key value to indicate a free entry in the cache. Alternatively there must be allowance for permitted and denied cache states – but this takes more storage.
#### Choice of Unique Key
The device/inode number pair is believed to give a unique identifier for each file. For local devices this is true but for smb mounts the inode number seems to be “faked” based on the file path.
Although device seems to be only 16 bits in size, 32 bits are returned by the stat interface. Similarly inode number is 32 bits, but this depends on file system type and reiserfs claims to be able to support 4294967295 inodes. (Note smb mounts claim to have 0 inodes.) So we end up with a 64 bit key.
Statistically, the inode number is likely to be allocated from 1 and the device to be a pair of bytes each allocated from 0. A key of inode=0 and device=-1 could be used as a marker for an empty entry.
The file path is also a candidate but is variable length and typically longer than 8 bytes. For local file systems, two names can be linked to the same inode. In addition, we do not trap renames so it would be possible to change the name of a virus file to that of a file already in the cache.
Keeping file lengths and/or mod times is not thought to be necessary.
#### Design Choices 1 – Key lookup
Much of the theory on caching is aimed at disk pages and modification of the LRU (Least Recently Used) algorithm. A big problem with these is that they have a data model where the data unit is large (a disk block at least) compared to the key (a 32 bit block number). First and second level memory caches come nearer to our case since the data and key sizes are more equal (although direct mapping reduces the key size).
If our case the data is small (1 bit) compared to the key (64 bits). Any history data or other overhead adds significantly to the cache size.
For example, doing LRU with a doubly linked list and a balanced tree search would treble the size of the cache data area. Comparing the performance graphs of a cache with 3n entries and one with n entries shows that any technique to improve performance must make impossible gains to justify the space needed.
The only mechanisms (I know of) that can do an efficient lookup without a space overhead are direct mapping and a simple unchained hash. (A chained hash would be better but the 50% space overhead is too expensive.)
While direct mapped n-way set-associative techniques are common in memory caches because of their simplicity, the overheads of a hash lookup are small as long as a simple hash is used (i.e. not a CRC based one) for significant pseudo-randomisation gain.
Similarly, conflict resolution by re-hash of the key with a limit of n on the number of tries is probably much better than n-way set associative (because the overflows of the first hash result do not conflict in most cases). The only argument against this might be that, say, a 4-way set associate cache could be done within the fetch size of the CPU.
#### Design Choices 2 – Replacement Strategy
Replacement strategy is a problem because of the same trade off between cache size and space. A 32bit time or counter value is unlikely to be cost effective, however a few bits might be possible. One way might be to structure the cache for speed as an array of 64 bit entries and a second array of bit, nibble or byte entries, giving a few bits for flags associated with cache usage or other things. If we need cache state flags for permit and deny then we might need a second array anyway. (The 1.5% space overhead per extra bit is very reasonable.)
It is difficult, however, to find good replacement strategies that are low overhead. A technique used by some memory cache hardware is to replace entry r (<n) and to increment r on each replacement. Theoretical studies based on random r have very good performance but it is difficult to get truly random numbers into a fast and simple algorithm. So sequential is used to give the longest repeat time. (Note the conflict lists are a map on the table and so an r per location is impractical.)
#### Suggested Algorithm
Choose a prime number m to be the number of cache entries kept. Choose a set size n and a prime number p such that n*p » m. Set r = 0. Keep st_dev and st_ino from the stat(2) return in an array of entries E[]. Initialise to –1,0 to represent no value stored.
Calculate the hash index j = (st_dev*st_ino)%m. (Note = ((st_dev%m)*(st_ino%m))%m.)
Set c = 0 and calculate the second hash s = (st_dev*st_ino)%p+1. (Note the +1 is important.)
Take a read lock and examine E[j]. If it matches we are done and if unused we must virus test (saving j and s if worthwhile).
If used but not matching then Examine E[(j+c*s)%m] for each c < n and make the same tests, if find none we must also virus test as above.
After virus test, if the result is permit (and not degraded or tentative), then we need to repeat the scan with a write lock to find either the first free entry (which we use), a match (ignore – someone checked the file in parallel) or not found. In the last case we overwrite the entry E[(j+(r%n)*s)%m] and increment r.
Set Size Choice (n)
For about 3000 unique entries in a 3000 entry table, you get the following fill ratios.
This shows that there is little gain for large set sizes. Since with a mature table the number of lookups is proportional to the set size, the smallest set size that gives reasonable performance is needed. This means n in the range 2 to 4, and I would choose n=2 for lowest cache overhead. (The same test showed a 100% fill ratio for 9390 files doing 16.5k matches.) There may be also an implementation gain for n=2 by removing the loop.
If you look forward to the next graph, there is a small gain by choosing n=3 so we need to compare the overheads with the gain. Note that I later repeated this test with about 25000 entries in a 25000 size table and, apart from n=1 (66%), the results were approximately the same.
Number of Cache Entries Choice (p)
Intuitively, the bigger the better. This graph shows the fill ratio for 10000 entries in different sizes of tables. (Note that fill is compared to table size or number of entries, whichever is the smaller.)
Another thing we can prove from this graph is that any technique which aimed to improve fill ratio at the expense of table size is doomed to failure. (Except in the artificial cases where there is enough free table space to absorb the overhead.) No point to the left of the 10k point is below 80%.
Some Statistical Results for Matching
I do not have time to do a proper statistical analysis of this, and therefore have used some sample data to prove that the algorithm works fairly well.
I think that repeat rates will be much lower than the sort of 80% usual for applications such as memory caches. Hence I have not considered anything lower than a 50% repeat rate. This simple test was done by mixing a random selection from a group of 1000 files with test data for 500000 files on a 1 in n basis with a 25k entry cache.
I actually did this for n=2 and n=3 but there were only 3 points that were 1% different, so the above is just the n=2 line.
Absolute Cache Size
If we assume that 200K bytes can be allocated to the cache, then that is 25K entries. Thus a choice for p is 24989; for n=2 s is 12491 and n=3 s is 8329. These give the following graph (Fill ratio as above.).
DECISION: To keep this away from the vetting controller.
Two-phase implementation
Phase 1	-	Simple check algorithm
Phase 2	-	Sophisticated in-progress check algorithm

#### Cache interface and implementation
Cache interface is designed to support four main operations which are find, add, clear, and purge. Implementation which implements that interface closely follows previously described algorithm. On top of that, standard IConfigurable interface is provided.
By default, cache starts disabled and with no configured cacheable filesystem types. Number of entries and set size are set to optimum values from theoretical discussion.

UMLDiagram 1Cache implementation

#### Cache Eval filter
Cache evaluation filter implements IInterceptFilter interface and is intended to be put in the evaluation chain with the StandardInterceptProcessor. It's purpose is to check whether the examined file is already present in the cache and allow access to it. It does that on the following way: upon invocation of the examineFile method, it extracts file's inode number and underlying block device major+minor numbers, and calls the find method from the ICache interface (which in turn checks if the file is present in the cache). Return code from that method determines the return code examineFile will give to the caller.
ExamineFilesystem is not implemented.

UMLDiagram 2Eval, Allow and Deny cache intercept filters

#### Cache Allow filter
Cache allow filter implements IInterceptFilter interface and is intended to be put in the allow chain with the StandardInterceptProcessor.
It implements two separate functionalities; if operation being examined is opening of a file in writeable mode, it will clear the entry from cache and return. Otherwise, if the file lies on the right filesystem, and if access to it was allowed by external (to the kernel modules) entity, allow decision will be cached.
ExamineFilesystem is used to purge all cached files from a given device upon unmount.

#### Cache Deny filter
Cache deny filter implements IInterceptFilter interface and is intended to be put in the deny chain with the StandardInterceptProcessor.
Only purpose of this filter is to delete cache entries when access to files is denied by external decision.
ExamineFilesystem is used to purge all cached files from a given device upon unmount.

#### Vetting Controller
The VettingController is at the heart of TALPA. It provides a framework for operations to be vetted by an external userspace client.
Essentially the internals of the VettingController are very similar to and are influenced by the Unix message queue design. Testing should the Unix message queue system was fast, however, it suffered a number of drawbacks – mainly related to failure scenarios (failure to cleanup stale data) and security (anyone can access it – provided they have the correct permissions and can exhaust/disrupt the transfer of data very easily). The most important area of the controller is the queue (mGroups[].intercepted), Which provides the basic fifo functionality.
The VettingController provides 8 groups of registered clients and intercepted operations will be routed to one of these groups (the default being group 0). Clients register with a group and will vet operations that are routed to the group.
 When the VettingController disabled existing requests will be serviced to completion.

The VettingController is, in essence, focused on mediating and coordinating the examine() methods invoked by the intercepted process and the obtainVettingDetails() and vettingResponse() methods invoked by the vetting clients.

Although normally this document will keep to a minimum the amount of information copied out of the model, the VettingController class, due to its importance in the system, has its documentation is reproduced in full here to aid understanding of its internal mechanisms.

public class: VettingController

Author:
Tvrtko A. Ursulin
Project:
Phase: 1.0; Status: Proposed; Version: 1.0; Complexity: 1
Dates:
Created: 21/04/2004 15:11:51; Modified: 07/02/2005 11:59:06;
Flags:
Active: false; IsRoot: false; IsLeaf: false;

The VettingController is an InterceptFilter that provides vetting of intercepted operations using 3rd party userspace clients.

Connections
Realisation <<realize>> link to interface [InterceptFilters].IInterceptFilter
Dependency link to class [VettingServer].TalpaPacket_FAIL
Dependency link to class [VettingServer].TalpaPacket_Register
Dependency link to class [VettingServer].TalpaPacket_Deregister
Dependency link to class [VettingServer].TalpaPacket_SetWaitTimeout
Dependency link to class [VettingServer].TalpaProtocolHeader
Dependency link to class [VettingServer].TalpaPacket_ObtainVettingDetails
Dependency link to class [VettingServer].TalpaPacket_VettingDetails
Dependency link to class [VettingServer].TalpaPacket_VettingResponse
Dependency link to class [VettingServer].TalpaPacketFragment_FileDetails
Dependency link to class [VettingServer].TalpaPacket_ExtDetailsOnly
Dependency link to class [VettingServer].TalpaPacket_OK
Dependency link to class [VettingServer].TalpaPacket_ExtVettingDetails
Dependency link to class [VettingServer].VettingClientID
Dependency link to class [VettingServer].TalpaPacket_FAIL
Dependency link to class [VettingServer].TalpaPacketFragment_ExtDetails
Realisation <<realize>> link to interface [VettingServer].IVettingServer
Aggregation link to class [VettingController].VettingGroup
Dependency link to class [VettingServer].TalpaPacketFragment_FilesystemDetails
Aggregation link from class [KernelModule-core].TALPA-core
Association link from class [VettingController].VettingClient
Association link from class [VettingController].VetCtrlConfigObject

VettingController Attributes

Attribute Details / private bool mEnabled / private talpa_simple_lock_t mVettingIDLock Notes: / Used for incrementing and getting the value of mNextVettingID. / private uint32 mNextVettingID Notes: / Forever incremening counter of vetting jobs. Used to give unique ID to individual jobs. / private talpa_rcu_lock_t mClientsLock Notes: / Protects the list of registered clients. / private VettingClientID mNextClientID Notes: / Forever incrementing counter of registered clients. Used to give them an unique Id at registration time. / private unsigned int[6] mFOPLookup Notes: / Lookup table which converts EFS_Open into TALPA_OPEN etc. / private talpa_rcu_lock_t mConfigLock Notes: / Protects the various configuration lists. / private talpa_mutex_t mConfigSerialise Notes: / Serialises userspace access through the configurator interface. / private atomic_t mTimeout Notes: / Wait for vetting response timeout value stored in jiffies. / private char* mRoutingsSet Notes: / Human readable representation of current routing configuration. Read out through configurator interface. / private IFilesystemFactory* mFilesystemFactory Notes: / Local pointer to the factory so that we dont have to go through the portability layer. / private IThreadAndProcessFactory* mThreadFactory Notes: / Local pointer to the factory so that we dont have to go through the portability layer.

VettingController Methods
Operation	Details
public examine( IEvaluationReport report, IPersonality userInfo, IFileInfo info, IFile file):void

Tags:	Implements=IInterceptFilter.examine ImplementsGuid={221FC7D6-E609-4804-8B43-CD230C1ACCC7}

	Notes:	Call excludeClient to avoid recursive interception. Call routeRequest to find out to which group this interception goes. If no group is found return immediately. Measure the lenght of various strings which will be put into packet and calculate the required packet size. Construct a IThreadInfo object and allocate memory for VettingDetails and for a vetting details packet. Fill in all the various details into the details and packet. Check if we got an IFile object and create one if not. Check if IFile object has an open file and try to open it if not. Return an error if the open fails. Get and increment the vetting id and increase the reference counts on the objects provided to us. Insert the details into the intercepted queue. Do proper locking while doing all of this. Finally wake up the clients registered in this group and call waitVettingResponse to wait for them. Call destroyVettingDetails and return.

public examine( IEvaluationReport report, IPersonality userInfo, IFilesystemInfo info):void	Sequential

Tags:	Implements=IInterceptFilter.examine ImplementsGuid={484A4455-451C-4aa5-BA9C-1AB286F2692E}
Notes:		Conceptually the same as the other examine method. The packets are different and there is no IFile object.

public enable():Boolean	Sequential

Tags:	Implements=IInterceptFilter.enable ImplementsGuid={0FC5107C-8FF9-459b-A834-DFF5E5CDBF55}
Notes:		The filter should be enabled. Returns: True if the filter was enabled by this call or was already enabled, else false.

public disable():void	Sequential

Tags:	Implements=IInterceptFilter.disable ImplementsGuid={64055C7C-71F1-4cbe-A625-BA737ECCC60A}
Notes:		Disable the filter.

public isEnabled():Boolean	Sequential

Tags:	Implements=IInterceptFilter.isEnabled ImplementsGuid={9A5EB194-67F7-40af-8E91-5DFF8EB56433}
Notes:		Determine if the filter is currently enabled. Returns: True if the filter is currently enabled, else false.

public queryMinPacketSize():unsigned int	Sequential

Tags:	Implements=IVettingServer.queryMinPacketSize ImplementsGuid={947D0301-1C9B-4ba3-9FBF-7299A918DD4F}
Notes:		Returns a minimum packet size in bytes that user can write into the interface.

public queryMaxPacketSize():unsigned int	Sequential

Tags:	Implements=IVettingServer.queryMaxPacketSize ImplementsGuid={BA19A272-EC5C-437e-B5A0-E5ED4847CDC2}

	Notes:	Returns a maximum packet size in bytes that user can write into the interface. This does not contain the potential stream payload but only the basic packet types.

public queryMinStreamPacket():unsigned int	Sequential

Tags:	Implements=IVettingServer.queryMinStreamPacket ImplementsGuid={690A17C2-CFFA-4f5b-9354-6FF1096F0D2D}
Notes:		Returns the minimum size of the stream packet+payload the implementation potentialy accepts.

public deregisterClient( VettingClient* client, TalpaPacket_Deregister packet):struct TalpaProtocolHeader*	Sequential

Tags:	Implements=IVettingServer.deregisterClient ImplementsGuid={E8510E8E-7EF7-4d46-9336-32D96529B93B}
Notes:		Deregister a client from the server. Returns: Either an OK or FAILresult packet as defined by the Vetting Client Protocol.

public queryMaxStreamPacket():unsigned int	Sequential

Tags:	Implements=IVettingServer.queryMaxStreamPacket ImplementsGuid={76232192-ADD7-4e55-91F2-6F9FBB9EAB99}
Notes:		Returns the maximum size of the stream packet+payload the implementation potentialy accepts.

public initializeClient():VettingClient*	Sequential

Tags:	Implements=IVettingServer.initializeClient ImplementsGuid={B0673E7C-9539-4854-8A9F-FD724E5D30DB}
Notes:		Allocates an VettingClient structure and sets the client to be unregistered. Fill in the process field. Sets the protocol version for response packets.

public processPacket( VettingClient* client, TalpaProtocolHeader* packet):struct TalpaProtocolHeader*	Sequential

Tags:	Implements=IVettingServer.processPacket ImplementsGuid={8782E5A2-9666-423f-8079-6BDE75FB86F7}

	Notes:	Serves as a main switchboard for received packets. Given any type of packet it knows what to do with it and calls the appropriate method. Returns a response packet if any.

public destroyClient( VettingClient* client):void	Sequential

Tags:	Implements=IVettingServer.destroyClient ImplementsGuid={A074B1BB-2CF7-4c39-BAB9-F53F4B29A1F6}
Notes:		Checks if the client is still registered, if so, emit a warning and forcefully deregister it. Free the VettingClient structure.

public setWaitTimeout( VettingClient* client, TalpaPacket_SetWaitTimeout packet):struct TalpaProtocolHeader*	Sequential

Tags:	Implements=IVettingServer.setWaitTimeout ImplementsGuid={09F349CA-136A-4354-AB9A-1BF2EEB038FF}
Notes:		Set the timeout that the client requires when attempting to obtain details. Timeout is either zero or a positive number. Then convert it to jiffies and store it for internal use. Returns: Either an OK or FAILresult packet as defined by the Vetting Client Protocol.

public peekVettingQueue( VettingClient* client):bool	Sequential

Tags:	Implements=IVettingServer.peekVettingQueue ImplementsGuid={A7FF2EF5-C530-4b10-9728-0CDC28CBF79B}
Notes:		Checks if there are pending vetting jobs for this client. Protects the list by taking the group lock.

public registerClient( VettingClient* client, TalpaPacket_Register packet):struct TalpaProtocolHeader*	Sequential

Tags:	Implements=IVettingServer.registerClient ImplementsGuid={2F7BA783-6B1D-46c8-86E8-A86CC8D5C81A}
Notes:		Register a vetting client with the server. Fails with -ECHRNG if group is out of range. Initialise fields in the VettingClient including client id (proper locking). Increments the number of registered clients in the group.

public obtainVettingDetails( VettingClient* client):struct TalpaProtocolHeader*	Sequential

Tags:	Implements=IVettingServer.obtainVettingDetails ImplementsGuid={4EF31704-C17B-4f00-AA88-70F552318BFC}

	Notes:	Obtain vetting, extended vetting, extended only details, or a stream data packets. If the client requested a stream operation, it will get the stream packet pending. If the client calls this after it has already requested extended details we do not have anything to give, so it will get -EBUSY. If the client is not currently vetting we will try to get him a new vetting job. Depending on the client preferences, it will either sleep or get -EAGAIN if there are no details available. Otherwise it will get the vetting details packet. If the vetting is already in progress we will interpret this as a request for the extended vetting details. Will try to construct one and give it to the client. Returns: A VettingDetails, ExtVettingDetails, or ExtDetailsOnly packet if data was available. If no data was available then the operation will block according to the timeout set. If the timeout was 0 the method returns FAIL immediately with the result set to EAGAIN. Otherwsie the operation will block. If the operation is interupted during blocking then FAIL will be sent and the error code set to EINTR, if a timeout is specified and this expires a FAIL will be returned with the error code set to EAGAIN. All other failures result in FAIL with error codes appropriately set.

public releaseVettingDetails( VettingClient* client):void	Sequential

Tags:	Implements=IVettingServer.releaseVettingDetails ImplementsGuid={4A4BAE70-E17C-4727-811F-DA82C2C49AF7}

	Notes:	After the client is finished with the packet obtained from obtainVettingDetails, it must release it! If it was a stream operation we will just reset the instream flag. If it was a job which doesn't require a response, we will consider this as a completion of this vetting and reset the client status and destroy the vetting details.

public streamReadAt( VettingClient* client, TalpaPacket_StreamReadAt* packet):struct TalpaProtocolHeader*	Sequential

Tags:	Implements=IVettingServer.streamReadAt ImplementsGuid={44D03DFA-38F8-4682-8BD4-BE5D1F04F885}
Notes:		Does a seek and then read, for possible scenarios see streamSeek and streamRead.

public vettingResponse( VettingClient* client, TalpaPacket_VettingResponse packet):struct TalpaProtocolHeader*	Sequential

Tags:	Implements=IVettingServer.vettingResponse ImplementsGuid={0093E981-700D-47b4-BDBE-C0BEFF4BF32B}

	Notes:	Inform the server of the client's response to a vetting. Depending on the response code from the packet, we will set the recommended action the the evaluation report. If the client wasn't supposed to respond, or did something wrong, we will return an appropriate error. If everything went fine, we will set the job as complete and wake up the process sleeping on the intercepted queue. Then we will reset the client since the vetting is now complete.

public streamLength( VettingClient* client):struct TalpaProtocolHeader*	Sequential

Tags:	Implements=IVettingServer.streamLength ImplementsGuid={58597B23-2A1E-43a1-9C2E-647F11A3414C}

	Notes:	If the stream is available returns the StreamData packet with the length of the stream as only payload. In the case of error returns a FAIL packet with the code returned the IFile->length. If the vetting is not in progress returns -ENOSR. If client doesn't have a vetting details assigned returns -EPIPE. If the file is not available returns -EBADF. If the file is not open returns -ENOSTR.

public streamWriteAt( VettingClient* client, TalpaPacket_StreamWriteAt* packet):struct TalpaProtocolHeader*	Sequential

Tags:	Implements=IVettingServer.streamWriteAt ImplementsGuid={7515CD9F-5CEE-4e9b-ABAA-4F173049A857}
Notes:		Does a seek and then read, for possible scenarios see streamSeek and streamRead.

public streamSeek( VettingClient* client, TalpaPacket_StreamSeek* packet):struct TalpaProtocolHeader*	Sequential

Tags:	Implements=IVettingServer.streamSeek ImplementsGuid={7D14B65E-BF16-4f89-995F-45C02F7CBC46}

	Notes:	If the stream is available returns the OK packet. In the case of error returns the FAIL packet with the code returned by the IFile->seek. If the vetting is not in progress returns -ENOSR. If client doesn't have a vetting details assigned returns -EPIPE. If the file is not available returns -EBADF. If the file is not open returns -ENOSTR.

public streamUnlinkFile( VettingClient* client, TalpaPacket_StreamUnlinkFile* packet):struct TalpaProtocolHeader*	Sequential

Tags:	Implements=IVettingServer.streamUnlinkFile ImplementsGuid={4F242B1F-1EB7-4de4-8FAB-01008197B75D}

	Notes:	If the stream is available, tries to unlink the file associated with it by calling IFile->unlink. Returns OK packet if successful or FAIL packet with the code returned. If the vetting is not in progress returns -ENOSR. If client doesn't have a vetting details assigned returns -EPIPE. If the file is not available returns -EBADF. If the file is not open returns -ENOSTR.

public streamRead( VettingClient* client, TalpaPacket_StreamRead* packet):struct TalpaProtocolHeader*	Sequential

Tags:	Implements=IVettingServer.streamRead ImplementsGuid={274372B0-7881-4533-8947-61D38FC1C9C8}

	Notes:	If the stream is available returns the StreamData packet. In the case of error returns a FAIL packet with the code returned from IFile->read. Actual bytes read is stored in the packet. Request for more than 128k - sizeof(struct TalpaPacket_StreamData) will return -EFBIG. If the vetting is not in progress returns -ENOSR. If client doesn't have a vetting details assigned returns -EPIPE. If the file is not available returns -EBADF. If the file is not open returns -ENOSTR.

public streamTruncate( VettingClient* client, TalpaPacket_StreamTruncate* packet):struct TalpaProtocolHeader*	Sequential

Tags:	Implements=IVettingServer.streamTruncate ImplementsGuid={1E274E71-F88B-4272-A14A-05D56E21B18E}

	Notes:	If the stream is available, tries to truncate it to the lenght given by calling IFile->truncate. Returns OK packet if successful or FAIL packet with the code returned. If the vetting is not in progress returns -ENOSR. If client doesn't have a vetting details assigned returns -EPIPE. If the file is not available returns -EBADF. If the file is not open returns -ENOSTR.

public streamWrite( VettingClient* client, TalpaPacket_StreamWrite* packet):struct TalpaProtocolHeader*	Sequential

Tags:	Implements=IVettingServer.streamWrite ImplementsGuid={F79F9C8A-C29C-4e0d-A0C8-E424DF0B5953}

	Notes:	If the stream is available returns the StreamData packet. Actual bytes written is stored in the packet. In the case of error returns a FAIL packet with the code returned from IFile->write. If the vetting is not in progress returns -ENOSR. If client doesn't have a vetting details assigned returns -EPIPE. If the file is not available returns -EBADF. If the file is not open returns -ENOSTR.

public streamReadAt( VettingClient* client, TalpaPacket_StreamReadAt packet):struct TalpaProtocolHeader*	Sequential

Tags:	Implements=IVettingServer.streamReadAt ImplementsGuid={44D03DFA-38F8-4682-8BD4-BE5D1F04F885}
Notes:		Does a seek and then read, for possible scenarios see streamSeek and streamRead.

public streamWriteAt( VettingClient* client, TalpaPacket_WriteAt packet):struct TalpaProtocolHeader*	Sequential

Tags:	Implements=IVettingServer.streamWriteAt ImplementsGuid={7515CD9F-5CEE-4e9b-ABAA-4F173049A857}
Notes:		Does a seek and then read, for possible scenarios see streamSeek and streamRead.

private routeRequest( char* path, unsigned int path_len, char* fstype, unsigned int fstype_len):VettingGroup*	Sequential

	Notes:	Take the config lock and iterate through the list of rules. Compare the path or filesystem with the each element until we find a match. If no rules did match, select group zero. Check if the selected group has any clients registered and if so, return the pointer to the group. Otherwise return NULL.

private waitVettingResponse( VettingGroup* group, VettingDetails* details, const char* filename):void	Sequential

	Notes:	Sleep on the intercepted queue until being woken up by vetting completion or a request to re-open the file. Also, sleep for a maximum of mTimeout jiffies. In the case vetting is complete set the externally vetted flag in the evaluation report and return. If the re-open was requested, re-open the file with read-write permissions and complete the reopen completion port. If we are woken up because the timeout expired unlink the job from the list (if still there) and set an error. If we were interrupted by an signal, set an -EINTR error.

private excludeClient():bool	Sequential

	Notes:	Take the clients lock and iterate throught the list of registerd clients. If the current process matches a client return true. Otherwhise return false. Always release the lock before return.

private newObject( EVetCtrlRoutingType type, const char* string, unsigned int group):VetCtrlConfigObject*	Sequential

Notes:			Notes for this method can be found in the filesystem exclusion processor.

private deleteObject( VetCtrlConfigObject* obj):void	Sequential

Notes:			Notes for this method can be found in the filesystem exclusion processor.

private constructStringSet( struct list_head* list, char** set):void	Sequential

Notes:			Notes for this method can be found in the filesystem exclusion processor.

private destroyStringSet( char** set):void	Sequential

Notes:			Notes for this method can be found in the filesystem exclusion processor.

private findObject( struct list_head* list, const char* value):VetCtrlConfigObject*	Sequential

Notes:			Notes for this method can be found in the filesystem exclusion processor.

private appendObject( struct list_head* list, EVetCtrlRoutingType type, const char* value, unsigned int group):VetCtrlConfigObject*	Sequential

Notes:			Notes for this method can be found in the filesystem exclusion processor.

private removeObject( struct list_head* list, const char* value):bool	Sequential

Notes:			Notes for this method can be found in the filesystem exclusion processor.

private doActionString( struct list_head* list, char** set, const char* value):void	Sequential

Notes:			Notes for this method can be found in the filesystem exclusion processor.

private static destroyVettingDetails( VettingDetails* details):void	Sequential

Notes:			Decrement and test the reference counts on vetting details object. If the last user is gone, destroy all the objects associated with it and finally free the details themselves.

private streamValidateRequest( VettingClient* client, VettingDetails* job):int	Sequential

Notes:			Called from all the stream functions the check the current vetting state. In different situations can return: -ENOSR: vetting is not in progress -EPIPE: no vetting details -EBADF: no file object -ENOSTR: file is not open

private setTimeout( const char* string):void	Sequential

	Notes:	Take the userspace supplied string, convert it to unsigned long value and then from milisecond to jiffies. Store it in mTimeout and in human readable string fetched by the configuration interface.

private static checkVettingQueue( VettingGroup* group):bool	Sequential

Notes:	Check whether there are some jobs on the groups intercepted list. If there is at least one returns true and DOES NOT RELEASE THE LOCK! The called must do that instead when done with the list. If there are no jobs releases the lock and returns false.

For clients the VettingController provides an IvettingServer interface. This may be used by clients to provide vetting services.

### SERVICE COMPONENTS
### Configurator
The Configurator is based loosely on the Observer (a.k.a Publish-Subscribe) design pattern[GAMMA].One of the primary aims of the configuration design is loose-coupling: avoidance of a single configuration object that is passed around the system – thus making all objects dependent on the configuration – and not reusable without it. The design shown allows a 3rd party piece of code to determine how objects should be configured; either the IConfigurable interface may invoked directly on any object that supports it, or the target object may be passed into an IConfigurator for 'anonymous-push' based conifguration.

HOW TO USE
IConfigurator
The Configurator is easy to use. Simply instantiate a concrete configurator. Objects that support IConfigurable may then attached to the configurator by invoking attach(). When configuration of an object is no longer required detach() may be called.
IConfigurable
An object that wishes to support configuration may do so by implementing the IConfigurable interface. It should be noted that the return from getAll() is a single dataset that exists for the lifetime of the object, and provides a read-only view of the object's configuration data.
It should be noted that to some degree this breaks encapsulation. However, it must be stressed that this read-only snapshot of the configuration does NOT necessarily represent the internal state of the object, and the configuration may also be stored separately in another appropriate form. However, the object must obey the constraint that 'Whenever its internal configuration changes, the changes are reflected immediately in the externalised representation'.
This situation has been deemed acceptable, thus avoiding having the object that implements this interface from telling observers about changes. Because of this it is intended that this externalisation of state
#### ProcfsConfigurator
The ProcfsConfigurator provides mediation between the sysctl/procfs and individual objects that implement an IConfigurable interface. This ultimately provides a highly-configurable but loosely-coupled configuration system.

IConfigurable objects are provided to the ProcfsConfigurator through the attach() method, and a removed from the configuration system via the dettach() method.
Every object that is attached to the configurator is allocated an ID and a reference stored in mItems.
The /proc directory will have the following structure:
/proc/sys/talpa/interceptors/<name>/<elements>
/proc/sys/talpa/intercept-processors/<name>/<elements>
/proc/sys/talpa/intercept-filters/<name>/<elements>
/proc/sys/talpa/filter-ifaces/<name>/<elements>
Where <name> is obtained from IConfigurable::getName() and the elements are defined on the list returned by IConfigurable::getAll(). The configuration data will be placed in a directory underneath /proc/sys/talpa, which is chosen in accordance with the EConfigurationGroup specified to the attach() method.
Internal data structures (configurationData) are used to support the operating system procfs. At no point is the IConfigurable object nor its internals exposed to the fact it is being configured by a procfs system. These structures are stored in mConfigurationData and will be allocated, reallocated, or deallocated as required in order to accommodate any attach()/detach() operations.
The procModify() and ctlModify() methods are used to change the configuration data. The information passed to these methods allows identification of the IConfigurable object, which will be located in mConfig. The IConfigurable::set() method will then be invoked, passing in the configuration name and the new value. It is this mechanism which allows anonymous modification of IConfigurable objects' configuration data. The ConfigurationElement::value string supplied via IConfigurable::getAll() is updated by the IConfigurable object. As the configurator already has a reference to the read-only data area – which was in turn passed onto procfs via the mConfigurationData data structures, the changes to the configuration (if any were indeed made – as validation may have refused the change) are immediately available.
### Operating System Services

#### SystemInterfaces
This package contains the main operating system interfaces. These typically will be any method used for IPC, or communicating with the kernel. However, these will ALWAYS be accessible via standard library calls.

TALPA currently only defines one system interface; IDeviceFile. This interface defines that methods that are supported by a device driver. They are pretty obvious in there meaning and therefore do not warrant further description here.
#### FileSystem
At kernel level different UNIX operating systems use different structures and mechanisms to support the implementation of various filesystem objects and the operations associated with those objects. TALPA core components need to be shielded from these differences and therefore the FileSystem package provides such an abstraction layer.

IFleInfo
This interface encapsulates the concept of a file, and the file resides on a particular device. Most operations are fairly obvious, however, the less obvious ones are described below:
getOperation()	- Returns the type of operation that was attempted on the file. This will be Open or Close.
isWriteable()	- Returns true if the file is currently open for write.
isWriteableAnywhere()	- Returns true if the file is currently open for write by ANY process on the system.
IFilesystemInfo
This interface encapsulates the concept of a Filesystem itself, again the filesystem resides on a particular device. Most operations are fairly obvious, however, the less obvious ones are described below:
getOperation()	- Returns the type of operation that was attempted on the file. This will be Mount or Unmount.
#### LinuxFilesystemImpl
The LinuxFilesystemImpl package provides Linux specific implementations of the Filesystem package.

#### Personality
Just like the Filesystem objects, the Personality encapsulate access to the different operating system kernel data structures. The Personality package focuses exclusively on user information such as their uid and group id.

IPersonality
This interface encapsulates the concept of a user. Most operations are fairly obvious and will not be described in this document. The model may examined if further information is necessary.
IPersonalityFactory
This factory interface only has one method: newPersonality(). The method will return the personality of the process that invoked the method.
#### LinuxPersonalityImpl
The LinuxPersonalityImpl package provides Linux specific implementations of the Personality package.

#### ProcessAndThread
This package is the counterpart to the Personality package. It encapsulates access to the different operating system kernel data structures. The ProcessAndThread package focuses exclusively on process and thread level information such as process id, parents, and its environment.

IThreadInfo
This interface encapsulates the concept of a thread. Most operations are fairly obvious and will not be described in this document. The model may examined if further information is necessary.
IProcessAndThreadFactory
This factory interface only has one method: newThreadInfo(). The method will return the information object for the thread that invoked the method.
#### LinuxProcessAndThreadImpl
The LinuxProcessAndThreadImpl package provides Linux specific implementations of the ProcessAndThread package. It is expected that the ThreadInfoImpl object is controlled by the factory as a singleton and that the methods will examine the operating system structures rather than store data.

FILTER INTERFACE COMPONENTS
### Process Exclusion Device Driver
The Process Exclusion Device Driver provides userspace with access to the Process Exclusion Processor through a standard operating system device file interface. The device major/minor numbers may be obtained from the configuration, as detailed in the appropriate section below.

Clients use this driver by opening the device. This open causes a registration with the ProcessExclusionProcessor. The client may then user ioctl(2) with the following request:
TLPPEIOC_IDLE
TLPPEIOC_ACTIVE
Setting the thread active will cause the whole process to be excluded from vetting, and conversely if set to idle the process operations will be vetted. When complete the thread simply closes the device, and a dereigster() will occur on the ProcessExclusionProcessor.
### Device Driver Vetting Client
The Device Driver Vetting Client provides a client to the VettingServer, presenting userspace processes with a device interface instead. It is based on the Adapter design pattern. It should be noted that the Vetting Client Protocol is implemented in a way such that a number of efficiencies are gained.

The use of the device interface presented by this class is described in detail in the interface specification section.
Because the interface is based on open files the device driver is notified whenever a daemon or other program exits (normal or abnormal). This allows the class to clean up after the abnormal termination of a daemon, thus creating increased stability – particularly in the case where the only or last remaining daemon is killed or terminates in an abnormal manner.
KERNEL-MODULE APPLICATION-CONTROL COMPONENTS
### General
Every system requires application-level system-specific entry and exit code to bootstrap, create and control the objects which form the system itself. For TALPA this application code is embodied in the Kernel-Module Application-Control components. If you like these are the glue between the various components in the system providing the bit of magic to make it all work by connecting the components up together.
These are the only components that may have dependencies on concrete components/classes. All other parts of the system must work with abstract interfaces ONLY. As these component know about the concrete objects they must also provide control, in particular singleton controls where appropriate.
Every kernel module that is produced is in fact an application-control component. Some component groups such as the 'Core' components only require a single kernel module, however, others should be delivered using a number of modules. Each module needs to conform the a template interface, which is component group specific. These interfaces are described below.
### Abstract Interfaces
The following Interfaces are realised by kernel-module components.

LinuxKernelModule
Method	Type	Notes
__init()	public: Integer	Provides initialisation of the module. Returns Z for success or NZ for failure.
__exit()	public: Integer	Clean up prior to unload of the module. Returns Z for success or NZ for failure.

ApplicationControl::ICoreApplicationControl
Method	Type	Notes
configurator()	public: IConfigurator	Returns the current configuration object.
interceptProcessor()	public: IInterceptProcessor	Returns the object that intercepts should be passed to.
vettingServer()	public: IVettingServer	Returns the current VettingController.
processExcluder()	public: IProcessExcluder	Returns the current ProcessExclusionProcessor.

ApplicationControl::IPortabilityApplicationControl
Method	Type	Notes
configurator()	public: IConfigurator	Returns a configurator interface.
systemRoot()	public: ISystemRoot	Returns a system root interface.
personalityFactory()	public: IPersonalityFactory	Returns a factory for the specific platform.
filesystemFactory()	public: IFilesystemFactory	Returns a factory for the specific platform.
threadandprocessFactory()	public: IThreadAndProcessFactory	Returns a factory for the specific platform.

### Intercept components: TALPA-syscall
EXPORTED INTERFACES
LinuxKernelModule
STRUCTURE

INTERFACE DETAILS
Method	Type	Notes
__init ()	public: Integer	Provides initialisation of the module. Creates a new SyscallInterceptImpl. Obtains the current InterceptProcessor from the TALPA-core and sets the SyscallInterceptImpl to target it. Obtains the current Configurator from the TALPA-core, and registers the SyscallInterceptImpl with it. Returns Z for success or NZ for failure.
__exit ()	public: Integer	Clean up prior to unload of the module. Deregisters th SyscallInterceptImpl from the Configurator. Deletes the SyscallInterceptImpl and returns Z for success or NZ for failure.

### Intercept components: TALPA-lsm
EXPORTED INTERFACES
LinuxKernelModule
STRUCTURE

INTERFACE DETAILS
Method	Type	Notes
__init ()	public: Integer	Provides initialisation of the module. Creates a new LSMInterceptImpl. Obtains the current InterceptProcessor from the TALPA-core and sets the LSMInterceptImpl to target it. Obtains the current Configurator from the TALPA-core, and registers the LSMInterceptImpl with it. Returns Z for success or NZ for failure.
__exit ()	public: Integer	Clean up prior to unload of the module. Deregisters the LSMInterceptImpl from the Configurator. Deletes the LSMInterceptImpl and returns Z for success or NZ for failure.

### Intercept components: TALPA-vfshook
EXPORTED INTERFACES
LinuxKernelModule
STRUCTURE

INTERFACE DETAILS

Method	Type	Notes
__init ()	public: Integer	Provides initialisation of the module. Creates a new LSMInterceptImpl. Obtains the current InterceptProcessor from the TALPA-core and sets the LSMInterceptImpl to target it. Obtains the current Configurator from the TALPA-core, and registers the LSMInterceptImpl with it. Returns Z for success or NZ for failure.
__exit ()	public: Integer	Clean up prior to unload of the module. Deregisters the LSMInterceptImpl from the Configurator. Deletes the LSMInterceptImpl and returns Z for success or NZ for failure.

### Core components: TALPA-core
EXPORTED INTERFACES
- Core-ApplicationControl
- LinuxKernelModule
STRUCTURE

INTERFACE DETAILS
Method	Type	Notes
__init ()	public: Integer	Creates a new StandardInterceptProcessor, ConifguratorProcFS, and the filters; CacheImpl, DegradedModeImpl, FilesystemObjectExcluderImpl, Lock ExcluderImpl and a VettingControllerImpl. Returns Z if everything initialised correctly else NZ. These objects are stored as attributes. The InterceptProcessor has all the filters added as appropriate, and finally all the objects are added to the Conifgurator.
__exit ()	public: Integer	The InterceptProcessor, InterceptFilters and Configurator objects will be removed from the system. Returns Z for succes or NZ if it is unable to unload.
configurator ()	public: Configurator	Returns mConfiguration.
interceptProcessor ()	public: InterceptProcessor	Returns mInterceptProcessorImpl.
vettingServer ()	public: VettingServer	Returns mVettingController.

### Core components: TALPA-linux
EXPORTED INTERFACES
- PortabilityApplicationControl
- LinuxKernelModule
STRUCTURE

INTERFACE DETAILS
Method	Type	Notes
__init ()	public: Integer	Provides initialisation of the module. Returns Z for success or NZ for failure.
__exit ()	public: Integer	Clean up prior to unload of the module. Returns Z for success or NZ for failure.
personalityFactory ()	public abstract: IPersonalityFactory	Returns a factory for the specific platform.
filesystemFactory ()	public abstract: IFilesystemFactory	Returns a factory for the specific platform.

### Filter interface components: TALPA-vcdevice
EXPORTED INTERFACES
LinuxKernelModule
STRUCTURE

INTERFACE DETAILS
Method	Type	Notes
__init ()	public: Integer	Provides initialisation of the module. Creates a new DeviceDriverVettingClient. Obtains the current VettingServer from the TALPA-core and sets the DeviceDriverVettingClient to target it. Obtains the current Configurator from the TALPA-core, and registers the DeviceDriverVettingClient with it. Returns Z for success or NZ for failure.
__exit ()	public: Integer	Clean up prior to unload of the module. Deregisters th DeviceDriverVettingClient from the Configurator. Deletes the DeviceDriverVettingClient and returns Z for success or NZ for failure.

### Filter interface components: TALPA-pedevice
EXPORTED INTERFACES
LinuxKernelModule
STRUCTURE

INTERFACE DETAILS
Method	Type	Notes
__init ()	public: Integer	Provides initialisation of the module. Creates a new ProcessExclusionDeviceDriver. Obtains the current ProcessExclusionProcessor from the TALPA-core and sets the ProcessExclusionDeviceDriver to target it. Returns Z for success or NZ for failure.
__exit ()	public: Integer	Clean up prior to unload of the module. Deletes the ProcessExclusionDeviceDriver and returns Z for success or NZ for failure.

# Dynamic behaviour
When looking at dynamic behaviour it should be remembered that there are two processes involved in each interception and there is no central core process controlling the system. Each dynamic behaviour can therefore be looked at from the either of the two perspectives (intercepted process or daemon) as well as from a complete end-to-end mechanism.

Initial load
Scenarios
Happy day
Excluded
Dynamic configuration
enable interception
disable interception
timeout during vetting
late response
deregister last vetting client
vetting client dies.

# Interface specification
Configuration & dynamic configuration
### General
Configurable Talpa components expose their configuration through the procfs and sysctl operating system interfaces. In procfs Talpa components may be found in the /proc/sys/talpa directory.
Configuration of Talpa may be achieved either by writing the appropriate values to procfs or alternatively via the sysctl(8) command line tool, or the sysctl(2) system call.
### Readable parameters
The following configuration parameters are available for read.
Component	Field	Values	Description
Interceptors
SyscallInterceptor	status enabled If enabled, the open, close, mount, umount, execve and libexec system calls are intercepted. / disabled No interception is being performed. / ops ±open ±close ±exec ±uselib ±mount ±umount Displays the list of intercepted system calls.
LSMInterceptor	status enabled If enabled, open, mount, umount, and execve are intercepted. / disabled No interception is being performed. / ops ±open ±close ±exec ±mount ±umount Displays the list of intercepted filesystem operations.
Intercept-processors
StandardInterceptProcessor	status	enabled The intercept processor is available for processing. / disabled The intercept processor is not available for processing.
Intercept-filters
SyslogFilter	status	enabled All interceptions will be logged to the system log. / disabled The filter is not active and no actions are performed.
DegradedModeProcessor	status enabled The processor is active and will provide pass-thru for root processes if the number of consecutive time-outs exceeds the configured threshold. / disabled The filter is not active and no actions are performed. / threshold <integer> The number of consecutive time-outs at or above which degraded mode is triggered. / Default: 3 / active true Degraded mode is currently active. / false Degraded mode is not active.
FilesystemInclusionProcessor	status enabled All operations on pathnames are checked against the include-path. If they reside outside the include path permission to continue the requested operation is immediately granted. / disabled The filter is not active and no actions are performed. / Include-path <path> The absolute path to a directory below which all operations will be vetted. / Default: /
FilesystemObjectExclusionProcessor	status enabled The exclusion processor will evaluate file-based operations against the list fo excluded items. If the operation details match one of the exclusions the operation is immediately granted. / disabled The filter is not active and no actions are performed. / fstypes <type> .. Contains one line per filesystem type name. An operation occurring on the type of filesystem which appears in this list will have permission granted without further vetting. / Default: procfs / paths <path> ... Contains one line per pathname. If the path ends in a / it is a directory and all operations at or below this directory will be excluded from vetting. / Default: none / mount-ftypes <type> .. Contains one line per filesystem type name. A mount or umount operation occurring on the type of filesystem which appears in this list will have permission granted without further vetting. / Default: procfs / mount-paths <path> ... Contains one line per mount device or mount point. If the path ends in a / it is a directory and all operations at or below this directory will be excluded from vetting. / Default: none / specials +dir ±symlink ±fifo ±socket ±bdev ±cdev This item contains 5 lines. Each line consists of a + or – symbol followed by a type of special file. A plus signifies that operations on these sorts of files are excluded from vetting. A minus sign indicates that they are included. / Default: +all
ProcessExclusionProcessor	status	enabled Process exclusions are enabled and any threads identified as active will be excluded from vetting whilst they remain active. / disabled The filter is not active and no actions are performed.
Cache	status enabled The cache will be used to increase performance on the specified filesystems. / disabled The filter is not active and no actions are performed. / fstypes <mount> ... Contains one line per mount point which is to be included in the cache. / Default: none. / stats <text> Contains cache statistics such as fill and hit ratio. / params <entries>,<prime>,<set-size> Current cache parameters, respectively: number of entries, prime number used by the algorithm, set size. / Default: 24989,12491,2
VettingController	status enabled Intercepted operations will will be made available to external applications for vetting. / disabled The filter is not active and no actions are performed. / routing fstype:<type>:<group> ... fs:<mount>:<group> ... Contains a list of routings. Filesystems which are not routed will be automatically routed to vetting client group 0. / The list is one routing per line. Filesystem-type routings will cause any operation on a filesystem of this type to be routed to the specified group. Filesystem routings will cause any operation on this particular filesystem to be routed to a particular group. Both fstype and fs routings may be intermingled. The order of precedence is top-down. / Default: none / timeout-ms <integer> The number of milliseconds that the VettingController will wait before cancelling the external vetting procedure for files. If the time-out for a given operation is exceeded the operation will be denied. / Default: 5000 / fs-timeout-ms <integer> The number of milliseconds that the VettingController will wait before cancelling the external vetting procedure for filesystems. If the time-out for a given operation is exceeded the operation will be denied. / Default: 60000 / xsmartsched-fix enabled / disabled Recent version of X server setup a timer (setitimer) for 20ms period which causes open()s to fail with -EINTR while scanning. Workaround disables the timer while userspace vetting is in progress.
OperationExclusionProcessor	status enabled Intercepted operations will be screened to remove write only or destructive open attempts. / disabled The filter is not active and no actions are performed. / fs-onlyblock enabled Mount or umount operations on non-block devices will not be intercepted. / disabled Mount or umount operations on non-block devices will be intercepted.
DenialSyslog	status	enabled All operation denials and the reason for the denial will be entered into the system log. / disabled The filter is not active and no actions are performed.
Device Drivers
VettingClientDeviceDriver	device	<major>,<minor>	The major/minor device numbers that may be used via a character device to communicate with the VettingServer.
ProcessExclusionDeviceDriver	device <major>,<minor> The major/minor device numbers that may be used via a character device to communicate with the ThreadExclusionProcessor. / deviceName <string> This is a placeholder for external data.

### Writeable parameters
The following configuration parameters are available. Some of the parameters may only be available if the component they are associated with is not currently enabled – this will be indicated against each configuration item below.
Component	Field	Values		Description
Interceptors
SyscallInterceptor	status enable The filter will be enabled. / disable The filter will be disabled. / ops ±open ±close ±exec ±uselib ±mount ±umount [Change when disabled] / Manipulates the bit mask of system calls to be hooked.
LSMInterceptor	status enable The filter will be enabled. / disable The filter will be disabled. / ops ±open ±close ±exec ±mount ±umount [Change when disabled] / Manipulates the bit mask of operations to be intercepted.
Intercept-processors
StandardInterceptProcessor	There are no writeable parameters.
Intercept-filters
SyslogFilter	status	enable The filter will be enabled. / disable The filter will be disabled.
DegradedModeProcessor	status enable The filter will be enabled. / disable The filter will be disabled. / threshold <integer> Sets the number of consecutive time-outs at, or above which degraded mode is active.
FilesystemInclusionProcessor	status enable The filter will be enabled. / disable The filter will be disabled. / Include-path <path> Sets the root directory of the directory hierarchy, within which operations will be vetted. If set to '/' then the filter will also be disabled.
FilesystemObjectExclusionProcessor	status enable The filter will be enabled. / disable The filter will be disabled. / fstypes +<type> The specified filesystem type will be added to the exclusions list. Any operation performed on this type of filesystem will be excluded from vetting. / -<type> The specified filesystem type will be removed from the exclusions list. Any operation performed on this type of filesystem will be vetted unless excluded by other means. / paths +<path> The specified directory hierarchy will be added to the exclusions list. Any operation performed on or below this directory will be excluded from vetting. / -<path> The specified directory hierarchy will be removed from the exclusions list. Any operation performed on or below this directory will be vetted unless excluded by other means. / mount-fstypes +<type> The specified filesystem type will be added to the exclusions list. Mount or umount operations performed on this type of filesystem will be excluded from vetting. / -<type> The specified filesystem type will be removed from the exclusions list. Mount or umount operations performed on this type of filesystem will be vetted unless excluded by other means. / mount-paths +<path> The specified directory hierarchy will be added to the exclusions list. Mount or umount operations performed on or below this directory will be excluded from vetting. / -<path> The specified directory hierarchy will be removed from the exclusions list. Mount or umount operations performed on or below this directory will be vetted unless excluded by other means. / specials +all All special files will be excluded from vetting. / -all All special files will be vetted unless excluded by other means. / +dir All directory files (the directory itself) will be excluded from vetting. / -dir All directory files (the directory itself) will be vetted unless excluded by other means. / +symlink All symbolic links will be excluded from vetting. / -symlink All symbolic links will be vetted unless excluded by other means. / +fifo All named pipes will be excluded from vetting. / -fifo All named pipes will be vetted unless excluded by other means. / +socket All bound sockets will be excluded from vetting. / -socket All bound sockets will be vetted unless excluded by other means. / +bdev All block devices will be excluded from vetting. / -bdev All block devices will be vetted unless excluded by other means. / +cdev All character devices will be excluded from vetting. / -cdev All character devices will be vetted unless excluded by other means.
ProcessExclusionProcessor	status	enable The filter will be enabled. / disable The filter will be disabled.
Cache	status enable The filter will be enabled. / disable The filter will be disabled. / enabled-fs +<mount> Adds the specified mount point to the list of filesystems for which caching of the external vetting result is enabled. / -<mount> Removes the specified mount point from the list of filesystems for which the external vetting result will be cached. / params <entries>[,<prime>[,<set-size>]] [Change when disabled] / Configures the cache parameters. Additional values are optional. Both incorrect or not given ones are automatically adjusted or calculated.
VettingController	status enable The filter will be enabled. / disable The filter will be disabled. / routing +fstype:<type>:<group> Operations on filesystems of the specified <type> will be routed to the vetting client group <group>. / -fstype:<type> The filesystem of the specified <type> will be removed from the routing table. / +fs:<mount>:<group> Operations on filesystem specified by <mount> will be routed to the vetting client group <group>. / -fs:<mount> The filesystem specified by <mount> will be removed from the routing table. / timeout-ms <integer> Sets the maximum permissible time that an external vetting procedure for files is allowed. / fs-timeout-ms <integer> Sets the maximum permissible time that an external vetting procedure for filesystems is allowed. / xsmartsched-fix enable / disable Recent version of X server setup a timer (setitimer) for 20ms period which causes open()s to fail with -EINTR while scanning. Workaround disables the timer while userspace vetting is in progress.
OperationExclusionProcessor	status enable The filter will be enabled. / disable The filter will be disabled. / fs-onlyblock enable Only mount operations on block devices will be intercepted. / disable All mount operations will be intercepted.
DenialSyslog	status	enable The filter will be enabled. / disable The filter will be disabled.
Device Drivers
VettingClientDeviceDriver	There are no writeable parameters.
ProcessExclusionDeviceDriver	deviceName		<string>		Arbitrary data can be written here.

TALPA Vetting Client Protocol
### General
The VettingServer provides a protocol that is designed to support a wide range of kernel-userspace communication technologies.
In common with many communication protocols it is based on a message being sent between a client and a server in either direction. The precise communication implementation technology will result in different representations of those messages (could be a simple function call or an actual packet over a bus-based mechanism such as the network loop-back). The data sent back and forth is represented by a packet, and a number of packets have been defined.
### Protocol Basics
The client connects to the server using a particular communication implementation; currently a device driver interface is supplied (DeviceDriverVettingClient). Once connected, the client registers and if necessary configures the connection – such as setting of the timeout. The client then continues to obtain vetting details and respond. When the client wishes to terminate the service it de-registers and closes the connection.
### Packet Basics
All packets are binary in format and contain a header and an optional payload. For ease of programming the packet may be accessed using C data structures. The structures are packed to avoid word-alignment issues resulting in gaps in the structure. This means that the 'block of memory' can be transmitted over simple serial communication mechanisms with relative ease, whilst still retaining a reasonable performance for programmatic access (the main cost being the in the fact that the structures may not be word-aligned – but the structures are designed to minimise such alignment issues).
It must be noted that data is represented using native byte-ordering, to enforce a particular byte-ordering scheme would resulting in an unnecessary performance overhead.
Each packet contains two data structures: a header and a payload. The header is a fixed structure with varying contents, the payload has both varying structure and contents depending upon the type of the packet.
#### Header Structure
All packets will be start with a header containing the following structure.
Type / uint32	Version / uint32	Payload-length / uint32

The 'Type' identifies both the packet meaning payload structure, and will be one of the following values.
Type Value	Packet Type	Programmatic Mnemonic
0x00000000	OK	TALPA_PKT_OK
0x00000001	FAIL	TALPA_PKT_FAIL
0x00000010	Register	TALPA_PKT_REG
0x00000020	Deregister	TALPA_PKT_DEREG
0x00000040	Set-Vetting-Timeout	TALPA_PKT_SETVETTIMEOUT
0x00000100	Obtain-Vetting-Details	TALPA_PKT_OBTAINVETDET
0x00001000	File-Details	TALPA_PKT_FILEDETAIL
0x00002000	Filesystem-Details	TALPA_PKT_FILESYSTEMDETAIL
0x00004000	Ext-Only-Details	TALPA_PKT_EXTVETDETAILONLY
0x00005000	Ext-File-Details	TALPA_PKT_EXTFILEDETAIL
0x00006000	Ext-Filesystem-Details	TALPA_PKT_EXTFILESYSTEMDETAIL
0x00010000	Vetting-Response	TALPA_PKT_VETRESPONSE
0x00100000	Stream-Data	TALPA_PKT_STREAMDATA
0x00100001	Stream-Length	TALPA_PKT_STREAMLENGTH
0x00100002	Stream-Seek	TALPA_PKT_STREAMSEEK
0x00100004	Stream-Read	TALPA_PKT_STREAMREAD
0x00100008	Stream-Write	TALPA_PKT_STREAMWRITE
0x00100014	Stream-Read-At	TALPA_PKT_STREAMREADAT
0x00100018	Stream-Write-At	TALPA_PKT_STREAMWRITEAT
0x00100020	Stream-Unlink-File	TALPA_PKT_STREAMUNLINKFILE
0x00100040	Stream-Truncate	TALPA_PKT_STREAMTRUNCATE

The 'Version' will be 0x00000002 for the current release of TALPA. Any change to ANY of the packets will result in a version number increase so that clients can support multi-versions of the protocol if necessary.
The 'Payload-length' is the length of the payload in bytes. This may be zero if the header conveys all of the required information.
### OK
The OK packet signifies that the previous operation was successful.
Payload
This packet does not have a payload, and therefore the 'Payload-length' will be set to 0.
### FAIL
The FAIL packet signifies that the previous operation was not successful.
Payload
Error-code / int32

Error-code	- Contains the error code of the failure. The error codes are based on errno.
### Register
The Register packet informs TALPA that the client wishes to receive vetting details and is willing to provide responses. The server will reply to a Register packet with either an OK packet if the client successfully registered or a FAIL packet if registration was not possible.
Payload
Group / uint32

Group	- An integer between 0 and 7 defining the vetting group that the client belongs to. Group 0 is the default group and will receive vetting details for all operations not routed to another group.
### De-register
The De-register packet informs TALPA that the client no-longer wishes to receive vetting details. The server will reply with either an OK packet if the client successfully de-registered or a FAIL packet if de-registration encountered an error.
Payload
This packet does not have a payload, and therefore the 'Payload-length' will be set to 0.
### Set-Wait-Timeout
This packet informs the VettingController of the maximum amount of time that the VettingController should wait for data to become available before responding to the client. The server will reply to a with either an OK packet if the timeout was accepted or a FAIL packet if an error was encountered.
Payload
Timeout-ms / uint32

Timeout-ms	- The maximum time in milliseconds that the VettingController should wait for data to become available before responding to the client. Setting a timeout of 0 means that the VettingController will never timeout and will always wait for data to become available.
### Obtain-Vetting-Details
The Obtain-Vetting-Details packet informs TALPA that the client wishes to receive vetting details. The server will reply with either a Vetting-Details or Ext-Vetting-Details packet or a FAIL packet if an error was encountered. If the client has specified a timeout, and Obtain-Vetting-Details exceeds this time, a FAIL packet is generated with EAGAIN set as the error-code. If Obtain-Vetting-Details is sent after a response requesting extended details then the response packet will be Ext-Details-Only (detailed below).
Payload
This packet does not have a payload, and therefore the 'Payload-length' will be set to 0.
Usage

### File/Filesystem Vetting-Details / Ext-Vetting-Details
The Vetting-Details and Ext-Vetting-Details packets provide information about a new vetting. The client is expected to perform whatever processing is required and then if required, respond with a decision.
Payload
The payload for this packet is the most complex with regard to the amount of information transmitted and the potential varying nature of the payload contents. Each packet starts with the following basic payload elements.
Vetting-ID / uint32	Response-reqd / uint32	ExtOffset / uint32_t

Vetting-ID	- The identifier for the vetting details.
Response-reqd	- This identifies whether or not the client has to respond with the result of the vetting. The value will be one of
ExtOffset	- Offset from the beginning of the payload where Extended Vetting Details start.
Resp.Req Value	Programmatic Mnemonic	Meaning
0x00000000	TALPA_DONTRESPOND	Vetting should be performed and no response should be sent to TALPA.
0x00000001	TALPA_RESPOND	Vetting should be performed and a response must be sent to TALPA.

Process-ID	- The process id of the thread attempting the operation.
Thread-ID	- The thread id of the thread attempting the operation.
The basic payload elements are then followed by the personality of the thread that is attempting the operation.
Uid / uid_t	Gid / gid_t	Euid / uid_t	Egid / gid_t	Fsuid / uid_t

Uid	- The real user id of the thread attempting the operation.
Gid	- The real group id of the thread attempting the operation.
Euid	- The effective user id of the thread attempting the operation.
Egid	- The effective group id of the thread attempting the operation.
Fsuid	- The filesystem user id of the thread attempting the operation. [Linux ONLY – else 0]
Following is the process/thread data.
Process-ID / pid_t	Thread-ID / tid_t

Process-ID	- The process id of the thread attempting the operation.
Thread-ID	- The thread id of the thread attempting the operation.
Following is the length of the process root directory.
RootDirLen / uint32_t

RootDirLen	- If the process is “chrooted” contains the length of the root directory part of the filename

Depending on the packet type, either file or filesystem details fragment can follow.
File Details

Operation / uint32	Flags / uint32	Mode / uint32	Filename / c-string

Operation	- Defines the operation that has been attempted on the file. This may be one of
Operation Value	Programmatic Mnemonic	Meaning
0x00000000	TALPA_OPEN	The file will be opened.
0x00000001	TALPA_CLOSE	The file will be closed.
0x00000002	TALPA_EXEC	The file will be executed.

Flags	- The flags passed to open(2).
Mode	- The mode pass to open(2).

Filesystem Details

Operation / uint32	FSType-offset / uint32	Device-offset / uint32	Mountpoint-offset / uint32	FSType / c-string	Device / c-string	Mountpoint / c-string

Operation	- Defines the operation that has been attempted on the file. This may be one of
Operation Value	Programmatic Mnemonic	Meaning
0x00000003	TALPA_MOUNT	The device will be mounted.
0x00000004	TALPA_UMOUNT	The mount point will be un-mounted.

Fstype-offset	- The offset from the start of the payload to the first byte of the Fs-type element.
Device-offset	- The offset from the start of the payload to the first byte of the Device-path element.
Mountpt-offset	- The offset from the start of the payload to the first byte of the Mount-point element.
Fs-type	- A string containing the name of the filesystem type.
Device-path	- A string defining the pathname of the device that is to be mounted.
Mount-point	- A string defining the directory onto which the filesystem should be mounted.

Finally, if no response is required then the extended vetting details will be appended to the packet. The payload will therefore contain the following additional elements.
Control-TTY / c-string	Env-length / uint32	Process-env / <Env-length> * bytes

Env-length	- The length in bytes of the Process-env element.
Process-env	- A BLOB containing the process environment suitable for use as an envp argument to exec(2).
Control-TTY	- A NUL-terminated string identifying the controlling terminal. If there is no terminal then the string will be empty and will consist of a single NUL byte.

Usage
As described under Obtain-Vetting-Details above, and the Vetting-Response below.
No response will be required for the following operations:
- Close
- umount
Normally the majority of operations will use a Vetting-Details packet due to the cost of obtaining the information in the extended details. Whenever a response is not required, the Ext-Vetting-Details packet will be sent instead of the Vetting-Details packet. This is because TALPA returns immediately to the calling process without waiting for a response from vetting.
### Vetting-Response
The Vetting-Response is sent by the client to indicate the result of vetting. The server will not respond to a Vetting-Response (response to a response?!).
Payload
Vetting-ID / uint32	Response / uint32

Vetting-ID	- The identifier for the vetting obtained from the original Vetting-Details packet.
Response	- The verdict of vetting. The response value will be one of the following
Response Value	Programmatic Mnemonic	Meaning
0x00000000	TALPA_ALLOW	The operation passed vetting and should be allowed.
0x00000001	TALPA_DENY	The operation failed vetting and should be denied.
0x00000002	TALPA_TIMEOUT	The vetting process timed-out whilst waiting on a resource and vetting could not be completed. The operation therefore should be denied.
0x00000003	TALPA_ERROR	An error occurred during vetting and the operation therefore should be reported as such.
0x00000004	TALPA_REQEXTDETAIL	Extended details are required.

If the response-type is TALPA-ERROR the payload will contain one additional element.
Error-code / int32

Error-code	- A numerical value based on errno indicating the nature of the error
Usage

### Ext-Details-Only
The Ext-Details-Only packet provides the client with extended information about the operation that is being vetted.
Payload
Control-TTY / c-string	Env-length / uint32	Process-env / <Env-length> * bytes

Env-length	- The length in bytes of the Process-env element.
Process-env	- A BLOB containing the process environment suitable for use as an envp argument to exec(2).
Control-TTY	- A NUL-terminated string identifying the controlling terminal. If there is no terminal then the string will be empty and will consist of a single NUL byte.
Usage
Described under Obtain-Vetting-Details above.

### StreamData
      The StreamData packet is sent to the client as a response to all of the stream packets except StreamSeek.
Payload
Size / uint64	<optional data> / uint8

Size	- The size in bytes of the optional data following.
Usage
Reported Size can be zero with no data following, or can be a number also with no data following. The later happens when StreamData is received as a response to StreamLength packet. Actual data available can be determined by looking at the payloadSize from the packet header and comparing it with Size.

### StreamLength
      Used to obtain the length of the file provided via I/O API.
      Carries no payload.
      Client will receive a StreamData packet with the stream size information as a response.
### StreamSeek
      Mimics the standard lseek(2) system call and is therefore used to modify the current file position.
Payload
Offset / int64	Mode / uint32

Offset	- Signed integer representing the amount of movement to be made
Mode	- On of: SEEK_CUR, SEEK_SET or SEEK_END to choose how to apply the Offset
Usage
    Client will receive an OK packet if the seek was successful, or a FAIL packet with the appropriate error code if it failed.
### StreamRead
      Request reading of data from the stream.
Payload
Size / uint32

Size	- Number of bytes to read
Usage
    Client will receive an StreamData packet with the at most Size bytes of data or a FAIL packet with an appropriate error code.
### StreamWrite
      Request reading of data from the stream.
Payload
Size / uint32	<data> / uint8

Size	- Number of bytes to write
Usage
    Client will receive an StreamData packet with the number of bytes actually written or a FAIL packet with an appropriate error code.
### StreamReadAt/StreamWriteAt
      Combines the functionality of StreamSeek and StreamRead or StreamWrite packet.
Payload
Size / uint32	Offset / int64	Mode / uint32	<optional data> / uint8

Size	- Number of bytes to read or to write
Offset	- Signed integer representing the amount of movement to be made
Mode	- On of: SEEK_CUR, SEEK_SET or SEEK_END to choose how to apply the Offset
Usage
    First the seek will be carried out, and if it fails, the client will receive a FAIL packet with an appropriate error code. Secondly, the actual read or write will be carried out and the return packet will be sent accordingly.
### StreamUnlinkFile
      Request the unlinking of the file associated with the stream.
      Carries no payload.
Usage
    Client will receive an OK packet with or a FAIL packet with an appropriate error code.
### StreamTruncate
      Request truncation of the file associated with the stream.
Payload
Length / uint64

Length	- Number of bytes to truncate to
Usage
    Client will receive an OK packet with or a FAIL packet with an appropriate error code.
TALPA Vetting Client (Device file)
### General
The current release of TALPA provides userspace clients with a device driver interface to the VettingController. Communications over this device are performed in accordance with the protocol defined above. This section is limited to describing the specifics of the device driver interface (DeviceDriverVettingClient) itself, and should be read in conjunction with the rest of the Interface specification.
### Protocol Notes
#### OK & FAIL
The functionality provided by these messages is instead replaced by use of the return code from the read, write and ioctl operations as defined by read(2), write(2) and ioctl(2). Typically, the operations will return
- OK: >= 0
- FAIL: -1, and errno will be appropriately set
This provides increased performance.
#### Obtain-Vetting-Details
This message is not to be sent. The act of performing the read() automatically provides this functionality. This provides increased performance.
#### Register/De-register/Set-Vetting-Timeout
These messages can also be performed via ioctl. The data passed to ioctl conforms to the protocol packet structures defined above. The response of OK or FAIL is available from the return code, as described above.
#### Writing the stream packets
        OK and FAIL packets which should be returned after requesting the stream operations will in fact return the appropriate return code directly to the write(2) system call.
### Open()
The open operation conforms to the behaviour specified in open(2). The file descriptor returned should be used for all subsequent operations. The mode must include O_RDWR.
### Write()
Write behaves normally and conforms to the behaviour specified in write(2). The data passed to the write() operation should be the protocol packet. The write() should be called only once per packet – passing the entire packet in one call. Multiple calls to write to output a complete a packet should not be performed and are not supported.
### Read()
Reads behave normally and conform to the behaviour specified in read(2). The client may make multiple calls to read to obtain the entire packet. This allows the client to allocate enough memory if necessary to read the payload.
The function will return with EAGAIN if the client uses blocking i/o and a vetting timeout > 0 has been set, and no vetting details become available during the specified time.
### Ioctl()
Used for register, deregister and setting the timeout for timed-blocking operations. The method conforms to the behaviour specified in ioctl(2).
### Close()
If the client was registered when the close is invoked the client is automatically de-registered. Should a multi-thread application terminate without cleaning up, the close() will be performed on each open file descriptor.
TALPA Process Exclusion (Device file)
TALPA thread exclusion is controlled by the ProcessExclusionProcessor. The TALPA filter-interface component talpa-pedevice provides device-driver based interface access to the filter. The interface and its semantics are defined below.
### Open
A standard open(2) system call. This will register the current process with the process exclusion processor. The device major/minor numbers may be obtained from the TALPA configuration as detailed below. Once the open successfully completes the thread may use ioctl(2) system calls to request process exclusion participation.
### Close
A standard close(2) system call passing in the file descriptor returned by invoking open(2) on the TALPA process exclusion device. The process will be de-registered with the exclusion processor. It does not matter if the process is currently considered active and excluded from vetting.
### IOCTL: Active
This standard ioctl(2) is invoked by:
ioctl(fd, TLPPEIOC_ACTIVE);
The file descriptor passed in must have previously been returned from a successful open(2) as described above. The process invoking the ioctl() method will be excluded from vetting. It is intended that an active-idle pairing protects only the filesystem operations that are sensitive to, and therefore should be excluded from vetting.
### IOCTL: idle
This standard ioctl(2) is invoked by:
ioctl(fd, TLPPEIOC_IDLE);
The file descriptor passed in must have previously been returned from a successful open(2) as described above. The process invoking the ioctl() method will be vetted as normal.
# Extending TALPA
Interceptor
[---- Existing code modified: NONE ----]
Integration of a new interceptor is relatively easy. The following simple steps should be followed:
- Create the interceptor source that provides both Interceptor and ConfigurationEntity interfaces.
- Create a kernel module. Initialisation of the kernel module should
- Create a new Interceptor object.
- Obtain from the core a reference to an InterceptProcessor.
- Set the new Interceptor to target the InterceptProcessor.
- Obtain from the core a reference to the Configurator.
- Add the new Interceptor to the Configurator.
No other files or components need to be amended.
Intercept filters
[---- Existing code modified: 1 file ----]
Intercept filters are generally added to the core components, and thus the addition of a new intercept filter is a little more involved that either a new vetting client or interceptor. However, the code changes are minimal and are confined to the core component kernel module code itself (basically 1 source file).
The following simple steps should be followed:
- Create the intercept filter source that provides both InterceptFilter and ConfigurationEntity interfaces.
- Amend the core component kernel module. The initialisation of the kernel module should include
- Creation of the new InterceptFilter object.
- Adding the new filter to the InterceptProcessor, so that is it evaluated at an appropriate point.
- Adding the new filter to the Configurator.
No other files or components need to be amended.
Vetting clients
### Interface presentation
[---- Existing code modified: NONE ----]
Currently there is only one client, DeviceDriverVettingClient. TALPA has been designed to be extensible and any number of interfaces could be implemented from sockets and message queues to shared memory, indeed one possible future enhancement is to produce a Dazuko2CompatibilityClient.
As described above any number of different vetting client interface modules may be used concurrently.
Just like adding a new Interceptor, adding a new vetting client interface is relatively easy. As the vetting client is based on the Adapter pattern[GAMMA], it is a straightforward case of adapting the VettingServer interface into another form.
The following simple steps should be followed:
- Create the client source that provides a ConfigurationEntity interface.
- Create a kernel module. Initialisation of the kernel module should
- Create the new vetting client interface object.
- Obtain from the core a reference to a VettingController.
- Set the new vetting client interface to target the VettingController.
- Obtain from the core a reference to the Configurator.
- Add the new vetting client interface to the Configurator.
No other files or components need to be amended.
# Future Possibilities
General
Please take heed that what is presented here is merely a list of possible ideas and may have had little or no exploration. They are recorded here in order to provide prosperity and longevity.
NOTE: The inclusion of ideas here should in no way be taken a a reflection of future direction, functionality or performance.
Architecture
Synopsis
All intercept filters (& other core components) could be packaged as individual kernel modules.
Description
Extending the filter and configuration systems to individually loaded modules would result in a totally extensible system.
Immediate thoughts
- This has particularly interesting possibilities regarding modularity, and source code stability – particularly with regard to the core component kernel module object.
- Performance would remain unaffected, as symbols would be resolved at time of load. Dynamically the code would operate as though it was in a single package but without the code dependencies.
Performance
### Vetting client/controller
Synopsis
Use of new read() from client to infer the result of the last read() was allowed.
Description
A performance enhancement may be possible where a daemon performs no actions between a write() of a successful vetting response and the next read() for another vetting request. If the assumption is that 99.99% of vetting results in ALLOW an extra call and the time associated with it may be saved.
Immediate thoughts
- Possible performance issue in round-trip times between vetting completing after a read and the next read occurring – it may be that some user-mode daemons perform actions which degrade performance or indeed result in no reply at all – this may be switchable in code or the daemon may optionally provide a write() for the case of no following read().
- Would need to store the last pending request so that the inferred reply could be made without further lookup.
# Known limitations
Overview
The section describes any known issues with the design or the architectural components.
Intercept components
Synopsis
Use of in-kernel NFS server will bypass scanning for remote clients.
Module
talpa-syscall
Operating systems
All Linux 2.4 kernels
Description
The design of the in-kernel NFS server (knfsd) is such that it does not use the standard system calls. This means that operations such as open and close by remote machines will not be intercepted. This leaves a medium-level security risk – relying on client protection only.
Resolution/work-around
Do not use the in-kernel NFS server – use a user-mode daemon used as rpc.nfsd instead. The knfsd is normally used for performance reasons. The decision to continue using knfsd would be at the expense of security, and would therefore pose a security risk. Alternatively another hooking mechanism could be employed which does not suffer these limitations. Use another hook mechanism such as RSBAC (talpa-rsbac) or Kernel Hooks (talpa-khooks).
Future outlook
This issue will continue to exist and will not be resolved.
Synopsis
Symlink accesses are reported as full paths.
Module
talpa-linux
Operating systems
All Linux kernels
Description
There is no way to resolve the original symlink from an open file. Therefore, the real path is always reported.
Resolution/work-around
No workaround.
Future outlook
This is unlikely to change.
Synopsis
The following sequence of operations is known to happen: creat-1, link1-2, unlink-1, write-1, close-1. Interception of the close operation is not able to produce the new filename.
Module
talpa-linux, talpa-core
Operating systems
All Linux kernels
Description
There is no way to determine where the file might be linked to without employing a complicated state keeping infrastructure and intercepting the link/unlink system calls. I/O API will provide the correct file for scanning, but the filename will not be correct. Therefore we can not alert the user about a possible threat being written into the file.
Resolution/work-around
This is not a security issue since the threat will be detected on the next access to the newly created file. Therefore no resolution is necessary..
Future outlook
This is unlikely to change.
Filter interface components
None.
Core components
None.
# Licensing
Introduction
This section describes the licenses under which TALPA is distributed. It provides a single point of reference for licensing questions, and includes copies of the actual licences used (section 7.2) and the full term terms of the licences (sections 7.3-7.5) as well.
Licenses
### Summary
The following table provides a summary of the licences used across the TALPA project and their scope.
Scope	License
Kernel module source code	GNU General Public Licence v2
TALPA vetting client interface	New BSD Licence
Example code	New BSD Licence
Documentation and UML models	GNU Free Documentation Licence v1.2

### Kernel module source

© Copyright 2004 Sophos PLC.
This program is free software; you can redistribute it and/or modify it under the terms of the GNU General Public License Version 2 as published by the Free Software Foundation.
This program is distributed in the hope that it will be useful, but WITHOUT ANY WARRANTY; without even the implied warranty of MERCHANTABILITY or FITNESS FOR A PARTICULAR PURPOSE. See the GNU General Public License for more details.
You should have received a copy of the GNU General Public License along with this program; if not, write to the Free Software Foundation, Inc., 59 Temple Place, Suite 330, Boston, MA 02111-1307 USA

### TALPA vetting client interface

© Copyright 2004 Sophos PLC.
All rights reserved.

Redistribution and use in source and binary forms, with or without modification, are permitted provided that the following conditions are met:
* Redistributions of source code must retain the above copyright notice, this list of conditions and the following disclaimer.
* Redistributions in binary form must reproduce the above copyright notice, this list of conditions and the following disclaimer in the documentation and/or other materials provided with the distribution.
* Neither the name of the Sophos nor the names of its contributors may be used to endorse or promote products derived from this software without specific prior written permission.
THIS SOFTWARE IS PROVIDED BY THE COPYRIGHT HOLDERS AND CONTRIBUTORS "AS IS" AND ANY EXPRESS OR IMPLIED WARRANTIES, INCLUDING, BUT NOT LIMITED TO, THE IMPLIED WARRANTIES OF MERCHANTABILITY AND FITNESS FOR A PARTICULAR PURPOSE ARE DISCLAIMED. IN NO EVENT SHALL THE COPYRIGHT OWNER OR CONTRIBUTORS BE LIABLE FOR ANY DIRECT, INDIRECT, INCIDENTAL, SPECIAL, EXEMPLARY, OR CONSEQUENTIAL DAMAGES (INCLUDING, BUT NOT LIMITED TO, PROCUREMENT OF SUBSTITUTE GOODS OR SERVICES; LOSS OF USE, DATA, OR PROFITS; OR BUSINESS INTERRUPTION) HOWEVER CAUSED AND ON ANY THEORY OF LIABILITY, WHETHER IN CONTRACT, STRICT LIABILITY, OR TORT (INCLUDING NEGLIGENCE OR OTHERWISE) ARISING IN ANY WAY OUT OF THE USE OF THIS SOFTWARE, EVEN IF ADVISED OF THE POSSIBILITY OF SUCH DAMAGE.

### Example code

© Copyright 2004 Sophos PLC.
All rights reserved.

Redistribution and use in source and binary forms, with or without modification, are permitted provided that the following conditions are met:
* Redistributions of source code must retain the above copyright notice, this list of conditions and the following disclaimer.
* Redistributions in binary form must reproduce the above copyright notice, this list of conditions and the following disclaimer in the documentation and/or other materials provided with the distribution.
* Neither the name of the Sophos nor the names of its contributors may be used to endorse or promote products derived from this software without specific prior written permission.
THIS SOFTWARE IS PROVIDED BY THE COPYRIGHT HOLDERS AND CONTRIBUTORS "AS IS" AND ANY EXPRESS OR IMPLIED WARRANTIES, INCLUDING, BUT NOT LIMITED TO, THE IMPLIED WARRANTIES OF MERCHANTABILITY AND FITNESS FOR A PARTICULAR PURPOSE ARE DISCLAIMED. IN NO EVENT SHALL THE COPYRIGHT OWNER OR CONTRIBUTORS BE LIABLE FOR ANY DIRECT, INDIRECT, INCIDENTAL, SPECIAL, EXEMPLARY, OR CONSEQUENTIAL DAMAGES (INCLUDING, BUT NOT LIMITED TO, PROCUREMENT OF SUBSTITUTE GOODS OR SERVICES; LOSS OF USE, DATA, OR PROFITS; OR BUSINESS INTERRUPTION) HOWEVER CAUSED AND ON ANY THEORY OF LIABILITY, WHETHER IN CONTRACT, STRICT LIABILITY, OR TORT (INCLUDING NEGLIGENCE OR OTHERWISE) ARISING IN ANY WAY OUT OF THE USE OF THIS SOFTWARE, EVEN IF ADVISED OF THE POSSIBILITY OF SUCH DAMAGE.

### Documentation and design Files

© Copyright 2004 Sophos PLC.
Permission is granted to copy, distribute and/or modify this document under the terms of the GNU Free Documentation License, Version 1.2 or any later version published by the Free Software Foundation; with no Invariant Sections, no Front-Cover Texts, and no Back-Cover Texts.
A copy of the license is included in the section entitled "GNU Free Documentation License".
GNU General Public Licence

GNU GENERAL PUBLIC LICENSE
Version 2, June 1991

Copyright (C) 1989, 1991 Free Software Foundation, Inc.
59 Temple Place - Suite 330, Boston, MA 02111-1307, USA
Everyone is permitted to copy and distribute verbatim copies of this license document, but changing it is not allowed.

Preamble
The licenses for most software are designed to take away your freedom to share and change it. By contrast, the GNU General Public License is intended to guarantee your freedom to share and change free software--to make sure the software is free for all its users. This General Public License applies to most of the Free Software Foundation's software and to any other program whose authors commit to using it. (Some other Free Software Foundation software is covered by the GNU Library General Public License instead.) You can apply it to your programs, too.
When we speak of free software, we are referring to freedom, not price. Our General Public Licenses are designed to make sure that you have the freedom to distribute copies of free software (and charge for this service if you wish), that you receive source code or can get it if you want it, that you can change the software or use pieces of it in new free programs; and that you know you can do these things.
To protect your rights, we need to make restrictions that forbid anyone to deny you these rights or to ask you to surrender the rights. These restrictions translate to certain responsibilities for you if you distribute copies of the software, or if you modify it.
For example, if you distribute copies of such a program, whether gratis or for a fee, you must give the recipients all the rights that you have. You must make sure that they, too, receive or can get the source code. And you must show them these terms so they know their rights.
We protect your rights with two steps: (1) copyright the software, and (2) offer you this license which gives you legal permission to copy, distribute and/or modify the software.
Also, for each author's protection and ours, we want to make certain that everyone understands that there is no warranty for this free software. If the software is modified by someone else and passed on, we want its recipients to know that what they have is not the original, so that any problems introduced by others will not reflect on the original authors' reputations.
Finally, any free program is threatened constantly by software patents. We wish to avoid the danger that redistributors of a free program will individually obtain patent licenses, in effect making the program proprietary. To prevent this, we have made it clear that any patent must be licensed for everyone's free use or not licensed at all.
The precise terms and conditions for copying, distribution and modification follow.
TERMS AND CONDITIONS FOR COPYING, DISTRIBUTION AND MODIFICATION
0. This License applies to any program or other work which contains a notice placed by the copyright holder saying it may be distributed under the terms of this General Public License. The "Program", below, refers to any such program or work, and a "work based on the Program" means either the Program or any derivative work under copyright law: that is to say, a work containing the Program or a portion of it, either verbatim or with modifications and/or translated into another language. (Hereinafter, translation is included without limitation in the term "modification".) Each licensee is addressed as "you".
Activities other than copying, distribution and modification are not covered by this License; they are outside its scope. The act of running the Program is not restricted, and the output from the Program is covered only if its contents constitute a work based on the Program (independent of having been made by running the Program). Whether that is true depends on what the Program does.
1. You may copy and distribute verbatim copies of the Program's source code as you receive it, in any medium, provided that you conspicuously and appropriately publish on each copy an appropriate copyright notice and disclaimer of warranty; keep intact all the notices that refer to this License and to the absence of any warranty; and give any other recipients of the Program a copy of this License along with the Program.
You may charge a fee for the physical act of transferring a copy, and you may at your option offer warranty protection in exchange for a fee.
2. You may modify your copy or copies of the Program or any portion of it, thus forming a work based on the Program, and copy and distribute such modifications or work under the terms of Section 1 above, provided that you also meet all of these conditions:
* a) You must cause the modified files to carry prominent notices stating that you changed the files and the date of any change.
* b) You must cause any work that you distribute or publish, that in whole or in part contains or is derived from the Program or any part thereof, to be licensed as a whole at no charge to all third parties under the terms of this License.
* c) If the modified program normally reads commands interactively when run, you must cause it, when started running for such interactive use in the most ordinary way, to print or display an announcement including an appropriate copyright notice and a notice that there is no warranty (or else, saying that you provide a warranty) and that users may redistribute the program under these conditions, and telling the user how to view a copy of this License. (Exception: if the Program itself is interactive but does not normally print such an announcement, your work based on the Program is not required to print an announcement.)
These requirements apply to the modified work as a whole. If identifiable sections of that work are not derived from the Program, and can be reasonably considered independent and separate works in themselves, then this License, and its terms, do not apply to those sections when you distribute them as separate works. But when you distribute the same sections as part of a whole which is a work based on the Program, the distribution of the whole must be on the terms of this License, whose permissions for other licensees extend to the entire whole, and thus to each and every part regardless of who wrote it.
Thus, it is not the intent of this section to claim rights or contest your rights to work written entirely by you; rather, the intent is to exercise the right to control the distribution of derivative or collective works based on the Program.
In addition, mere aggregation of another work not based on the Program with the Program (or with a work based on the Program) on a volume of a storage or distribution medium does not bring the other work under the scope of this License.
3. You may copy and distribute the Program (or a work based on it, under Section 2) in object code or executable form under the terms of Sections 1 and 2 above provided that you also do one of the following:
* a) Accompany it with the complete corresponding machine-readable source code, which must be distributed under the terms of Sections 1 and 2 above on a medium customarily used for software interchange; or,
* b) Accompany it with a written offer, valid for at least three years, to give any third party, for a charge no more than your cost of physically performing source distribution, a complete machine-readable copy of the corresponding source code, to be distributed under the terms of Sections 1 and 2 above on a medium customarily used for software interchange; or,
* c) Accompany it with the information you received as to the offer to distribute corresponding source code. (This alternative is allowed only for noncommercial distribution and only if you received the program in object code or executable form with such an offer, in accord with Subsection b above.)
The source code for a work means the preferred form of the work for making modifications to it. For an executable work, complete source code means all the source code for all modules it contains, plus any associated interface definition files, plus the scripts used to control compilation and installation of the executable. However, as a special exception, the source code distributed need not include anything that is normally distributed (in either source or binary form) with the major components (compiler, kernel, and so on) of the operating system on which the executable runs, unless that component itself accompanies the executable.
If distribution of executable or object code is made by offering access to copy from a designated place, then offering equivalent access to copy the source code from the same place counts as distribution of the source code, even though third parties are not compelled to copy the source along with the object code.
4. You may not copy, modify, sublicense, or distribute the Program except as expressly provided under this License. Any attempt otherwise to copy, modify, sublicense or distribute the Program is void, and will automatically terminate your rights under this License. However, parties who have received copies, or rights, from you under this License will not have their licenses terminated so long as such parties remain in full compliance.
5. You are not required to accept this License, since you have not signed it. However, nothing else grants you permission to modify or distribute the Program or its derivative works. These actions are prohibited by law if you do not accept this License. Therefore, by modifying or distributing the Program (or any work based on the Program), you indicate your acceptance of this License to do so, and all its terms and conditions for copying, distributing or modifying the Program or works based on it.
6. Each time you redistribute the Program (or any work based on the Program), the recipient automatically receives a license from the original licensor to copy, distribute or modify the Program subject to these terms and conditions. You may not impose any further restrictions on the recipients' exercise of the rights granted herein. You are not responsible for enforcing compliance by third parties to this License.
7. If, as a consequence of a court judgment or allegation of patent infringement or for any other reason (not limited to patent issues), conditions are imposed on you (whether by court order, agreement or otherwise) that contradict the conditions of this License, they do not excuse you from the conditions of this License. If you cannot distribute so as to satisfy simultaneously your obligations under this License and any other pertinent obligations, then as a consequence you may not distribute the Program at all. For example, if a patent license would not permit royalty-free redistribution of the Program by all those who receive copies directly or indirectly through you, then the only way you could satisfy both it and this License would be to refrain entirely from distribution of the Program.
If any portion of this section is held invalid or unenforceable under any particular circumstance, the balance of the section is intended to apply and the section as a whole is intended to apply in other circumstances.
It is not the purpose of this section to induce you to infringe any patents or other property right claims or to contest validity of any such claims; this section has the sole purpose of protecting the integrity of the free software distribution system, which is implemented by public license practices. Many people have made generous contributions to the wide range of software distributed through that system in reliance on consistent application of that system; it is up to the author/donor to decide if he or she is willing to distribute software through any other system and a licensee cannot impose that choice.
This section is intended to make thoroughly clear what is believed to be a consequence of the rest of this License.
8. If the distribution and/or use of the Program is restricted in certain countries either by patents or by copyrighted interfaces, the original copyright holder who places the Program under this License may add an explicit geographical distribution limitation excluding those countries, so that distribution is permitted only in or among countries not thus excluded. In such case, this License incorporates the limitation as if written in the body of this License.
9. The Free Software Foundation may publish revised and/or new versions of the General Public License from time to time. Such new versions will be similar in spirit to the present version, but may differ in detail to address new problems or concerns.
Each version is given a distinguishing version number. If the Program specifies a version number of this License which applies to it and "any later version", you have the option of following the terms and conditions either of that version or of any later version published by the Free Software Foundation. If the Program does not specify a version number of this License, you may choose any version ever published by the Free Software Foundation.
10. If you wish to incorporate parts of the Program into other free programs whose distribution conditions are different, write to the author to ask for permission. For software which is copyrighted by the Free Software Foundation, write to the Free Software Foundation; we sometimes make exceptions for this. Our decision will be guided by the two goals of preserving the free status of all derivatives of our free software and of promoting the sharing and reuse of software generally.
NO WARRANTY
11. BECAUSE THE PROGRAM IS LICENSED FREE OF CHARGE, THERE IS NO WARRANTY FOR THE PROGRAM, TO THE EXTENT PERMITTED BY APPLICABLE LAW. EXCEPT WHEN OTHERWISE STATED IN WRITING THE COPYRIGHT HOLDERS AND/OR OTHER PARTIES PROVIDE THE PROGRAM "AS IS" WITHOUT WARRANTY OF ANY KIND, EITHER EXPRESSED OR IMPLIED, INCLUDING, BUT NOT LIMITED TO, THE IMPLIED WARRANTIES OF MERCHANTABILITY AND FITNESS FOR A PARTICULAR PURPOSE. THE ENTIRE RISK AS TO THE QUALITY AND PERFORMANCE OF THE PROGRAM IS WITH YOU. SHOULD THE PROGRAM PROVE DEFECTIVE, YOU ASSUME THE COST OF ALL NECESSARY SERVICING, REPAIR OR CORRECTION.
12. IN NO EVENT UNLESS REQUIRED BY APPLICABLE LAW OR AGREED TO IN WRITING WILL ANY COPYRIGHT HOLDER, OR ANY OTHER PARTY WHO MAY MODIFY AND/OR REDISTRIBUTE THE PROGRAM AS PERMITTED ABOVE, BE LIABLE TO YOU FOR DAMAGES, INCLUDING ANY GENERAL, SPECIAL, INCIDENTAL OR CONSEQUENTIAL DAMAGES ARISING OUT OF THE USE OR INABILITY TO USE THE PROGRAM (INCLUDING BUT NOT LIMITED TO LOSS OF DATA OR DATA BEING RENDERED INACCURATE OR LOSSES SUSTAINED BY YOU OR THIRD PARTIES OR A FAILURE OF THE PROGRAM TO OPERATE WITH ANY OTHER PROGRAMS), EVEN IF SUCH HOLDER OR OTHER PARTY HAS BEEN ADVISED OF THE POSSIBILITY OF SUCH DAMAGES.
END OF TERMS AND CONDITIONS
GNU Free Documentation Licence

GNU Free Documentation License
Version 1.2, November 2002

Copyright (C) 2000,2001,2002 Free Software Foundation, Inc.
59 Temple Place, Suite 330, Boston, MA 02111-1307 USA
Everyone is permitted to copy and distribute verbatim copies of this license document, but changing it is not allowed.

0. PREAMBLE
The purpose of this License is to make a manual, textbook, or other functional and useful document "free" in the sense of freedom: to assure everyone the effective freedom to copy and redistribute it, with or without modifying it, either commercially or noncommercially. Secondarily, this License preserves for the author and publisher a way to get credit for their work, while not being considered responsible for modifications made by others.
This License is a kind of "copyleft", which means that derivative works of the document must themselves be free in the same sense. It complements the GNU General Public License, which is a copyleft license designed for free software.
We have designed this License in order to use it for manuals for free software, because free software needs free documentation: a free program should come with manuals providing the same freedoms that the software does. But this License is not limited to software manuals; it can be used for any textual work, regardless of subject matter or whether it is published as a printed book. We recommend this License principally for works whose purpose is instruction or reference.
1. APPLICABILITY AND DEFINITIONS
This License applies to any manual or other work, in any medium, that contains a notice placed by the copyright holder saying it can be distributed under the terms of this License. Such a notice grants a world-wide, royalty-free license, unlimited in duration, to use that work under the conditions stated herein. The "Document", below, refers to any such manual or work. Any member of the public is a licensee, and is addressed as "you". You accept the license if you copy, modify or distribute the work in a way requiring permission under copyright law.
A "Modified Version" of the Document means any work containing the Document or a portion of it, either copied verbatim, or with modifications and/or translated into another language.
A "Secondary Section" is a named appendix or a front-matter section of the Document that deals exclusively with the relationship of the publishers or authors of the Document to the Document's overall subject (or to related matters) and contains nothing that could fall directly within that overall subject. (Thus, if the Document is in part a textbook of mathematics, a Secondary Section may not explain any mathematics.) The relationship could be a matter of historical connection with the subject or with related matters, or of legal, commercial, philosophical, ethical or political position regarding them.
The "Invariant Sections" are certain Secondary Sections whose titles are designated, as being those of Invariant Sections, in the notice that says that the Document is released under this License. If a section does not fit the above definition of Secondary then it is not allowed to be designated as Invariant. The Document may contain zero Invariant Sections. If the Document does not identify any Invariant Sections then there are none.
The "Cover Texts" are certain short passages of text that are listed, as Front-Cover Texts or Back-Cover Texts, in the notice that says that the Document is released under this License. A Front-Cover Text may be at most 5 words, and a Back-Cover Text may be at most 25 words.
A "Transparent" copy of the Document means a machine-readable copy, represented in a format whose specification is available to the general public, that is suitable for revising the document straightforwardly with generic text editors or (for images composed of pixels) generic paint programs or (for drawings) some widely available drawing editor, and that is suitable for input to text formatters or for automatic translation to a variety of formats suitable for input to text formatters. A copy made in an otherwise Transparent file format whose markup, or absence of markup, has been arranged to thwart or discourage subsequent modification by readers is not Transparent. An image format is not Transparent if used for any substantial amount of text. A copy that is not "Transparent" is called "Opaque".
Examples of suitable formats for Transparent copies include plain ASCII without markup, Texinfo input format, LaTeX input format, SGML or XML using a publicly available DTD, and standard-conforming simple HTML, PostScript or PDF designed for human modification. Examples of transparent image formats include PNG, XCF and JPG. Opaque formats include proprietary formats that can be read and edited only by proprietary word processors, SGML or XML for which the DTD and/or processing tools are not generally available, and the machine-generated HTML, PostScript or PDF produced by some word processors for output purposes only.
The "Title Page" means, for a printed book, the title page itself, plus such following pages as are needed to hold, legibly, the material this License requires to appear in the title page. For works in formats which do not have any title page as such, "Title Page" means the text near the most prominent appearance of the work's title, preceding the beginning of the body of the text.
A section "Entitled XYZ" means a named subunit of the Document whose title either is precisely XYZ or contains XYZ in parentheses following text that translates XYZ in another language. (Here XYZ stands for a specific section name mentioned below, such as "Acknowledgements", "Dedications", "Endorsements", or "History".) To "Preserve the Title" of such a section when you modify the Document means that it remains a section "Entitled XYZ" according to this definition.
The Document may include Warranty Disclaimers next to the notice which states that this License applies to the Document. These Warranty Disclaimers are considered to be included by reference in this License, but only as regards disclaiming warranties: any other implication that these Warranty Disclaimers may have is void and has no effect on the meaning of this License.
2. VERBATIM COPYING
You may copy and distribute the Document in any medium, either commercially or noncommercially, provided that this License, the copyright notices, and the license notice saying this License applies to the Document are reproduced in all copies, and that you add no other conditions whatsoever to those of this License. You may not use technical measures to obstruct or control the reading or further copying of the copies you make or distribute. However, you may accept compensation in exchange for copies. If you distribute a large enough number of copies you must also follow the conditions in section 3.
You may also lend copies, under the same conditions stated above, and you may publicly display copies.
3. COPYING IN QUANTITY
If you publish printed copies (or copies in media that commonly have printed covers) of the Document, numbering more than 100, and the Document's license notice requires Cover Texts, you must enclose the copies in covers that carry, clearly and legibly, all these Cover Texts: Front-Cover Texts on the front cover, and Back-Cover Texts on the back cover. Both covers must also clearly and legibly identify you as the publisher of these copies. The front cover must present the full title with all words of the title equally prominent and visible. You may add other material on the covers in addition. Copying with changes limited to the covers, as long as they preserve the title of the Document and satisfy these conditions, can be treated as verbatim copying in other respects.
If the required texts for either cover are too voluminous to fit legibly, you should put the first ones listed (as many as fit reasonably) on the actual cover, and continue the rest onto adjacent pages.
If you publish or distribute Opaque copies of the Document numbering more than 100, you must either include a machine-readable Transparent copy along with each Opaque copy, or state in or with each Opaque copy a computer-network location from which the general network-using public has access to download using public-standard network protocols a complete Transparent copy of the Document, free of added material. If you use the latter option, you must take reasonably prudent steps, when you begin distribution of Opaque copies in quantity, to ensure that this Transparent copy will remain thus accessible at the stated location until at least one year after the last time you distribute an Opaque copy (directly or through your agents or retailers) of that edition to the public.
It is requested, but not required, that you contact the authors of the Document well before redistributing any large number of copies, to give them a chance to provide you with an updated version of the Document.
4. MODIFICATIONS
You may copy and distribute a Modified Version of the Document under the conditions of sections 2 and 3 above, provided that you release the Modified Version under precisely this License, with the Modified Version filling the role of the Document, thus licensing distribution and modification of the Modified Version to whoever possesses a copy of it. In addition, you must do these things in the Modified Version:
A. Use in the Title Page (and on the covers, if any) a title distinct from that of the Document, and from those of previous versions (which should, if there were any, be listed in the History section of the Document). You may use the same title as a previous version if the original publisher of that version gives permission.
B. List on the Title Page, as authors, one or more persons or entities responsible for authorship of the modifications in the Modified Version, together with at least five of the principal authors of the Document (all of its principal authors, if it has fewer than five), unless they release you from this requirement.
C. State on the Title page the name of the publisher of the Modified Version, as the publisher.
D. Preserve all the copyright notices of the Document.
E. Add an appropriate copyright notice for your modifications adjacent to the other copyright notices.
F. Include, immediately after the copyright notices, a license notice giving the public permission to use the Modified Version under the terms of this License, in the form shown in the Addendum below.
G. Preserve in that license notice the full lists of Invariant Sections and required Cover Texts given in the Document's license notice.
H. Include an unaltered copy of this License.
I. Preserve the section Entitled "History", Preserve its Title, and add to it an item stating at least the title, year, new authors, and publisher of the Modified Version as given on the Title Page. If there is no section Entitled "History" in the Document, create one stating the title, year, authors, and publisher of the Document as given on its Title Page, then add an item describing the Modified Version as stated in the previous sentence.
J. Preserve the network location, if any, given in the Document for public access to a Transparent copy of the Document, and likewise the network locations given in the Document for previous versions it was based on. These may be placed in the "History" section. You may omit a network location for a work that was published at least four years before the Document itself, or if the original publisher of the version it refers to gives permission.
K. For any section Entitled "Acknowledgements" or "Dedications", Preserve the Title of the section, and preserve in the section all the substance and tone of each of the contributor acknowledgements and/or dedications given therein.
L. Preserve all the Invariant Sections of the Document, unaltered in their text and in their titles. Section numbers or the equivalent are not considered part of the section titles.
M. Delete any section Entitled "Endorsements". Such a section may not be included in the Modified Version.
N. Do not retitle any existing section to be Entitled "Endorsements" or to conflict in title with any Invariant Section.
O. Preserve any Warranty Disclaimers.
If the Modified Version includes new front-matter sections or appendices that qualify as Secondary Sections and contain no material copied from the Document, you may at your option designate some or all of these sections as invariant. To do this, add their titles to the list of Invariant Sections in the Modified Version's license notice. These titles must be distinct from any other section titles.
You may add a section Entitled "Endorsements", provided it contains nothing but endorsements of your Modified Version by various parties--for example, statements of peer review or that the text has been approved by an organization as the authoritative definition of a standard.
You may add a passage of up to five words as a Front-Cover Text, and a passage of up to 25 words as a Back-Cover Text, to the end of the list of Cover Texts in the Modified Version. Only one passage of Front-Cover Text and one of Back-Cover Text may be added by (or through arrangements made by) any one entity. If the Document already includes a cover text for the same cover, previously added by you or by arrangement made by the same entity you are acting on behalf of, you may not add another; but you may replace the old one, on explicit permission from the previous publisher that added the old one.
The author(s) and publisher(s) of the Document do not by this License give permission to use their names for publicity for or to assert or imply endorsement of any Modified Version.
5. COMBINING DOCUMENTS
You may combine the Document with other documents released under this License, under the terms defined in section 4 above for modified versions, provided that you include in the combination all of the Invariant Sections of all of the original documents, unmodified, and list them all as Invariant Sections of your combined work in its license notice, and that you preserve all their Warranty Disclaimers.
The combined work need only contain one copy of this License, and multiple identical Invariant Sections may be replaced with a single copy. If there are multiple Invariant Sections with the same name but different contents, make the title of each such section unique by adding at the end of it, in parentheses, the name of the original author or publisher of that section if known, or else a unique number. Make the same adjustment to the section titles in the list of Invariant Sections in the license notice of the combined work.
In the combination, you must combine any sections Entitled "History" in the various original documents, forming one section Entitled "History"; likewise combine any sections Entitled "Acknowledgements", and any sections Entitled "Dedications". You must delete all sections Entitled "Endorsements".
6. COLLECTIONS OF DOCUMENTS
You may make a collection consisting of the Document and other documents released under this License, and replace the individual copies of this License in the various documents with a single copy that is included in the collection, provided that you follow the rules of this License for verbatim copying of each of the documents in all other respects.
You may extract a single document from such a collection, and distribute it individually under this License, provided you insert a copy of this License into the extracted document, and follow this License in all other respects regarding verbatim copying of that document.
7. AGGREGATION WITH INDEPENDENT WORKS
A compilation of the Document or its derivatives with other separate and independent documents or works, in or on a volume of a storage or distribution medium, is called an "aggregate" if the copyright resulting from the compilation is not used to limit the legal rights of the compilation's users beyond what the individual works permit. When the Document is included in an aggregate, this License does not apply to the other works in the aggregate which are not themselves derivative works of the Document.
If the Cover Text requirement of section 3 is applicable to these copies of the Document, then if the Document is less than one half of the entire aggregate, the Document's Cover Texts may be placed on covers that bracket the Document within the aggregate, or the electronic equivalent of covers if the Document is in electronic form. Otherwise they must appear on printed covers that bracket the whole aggregate.
8. TRANSLATION
Translation is considered a kind of modification, so you may distribute translations of the Document under the terms of section 4. Replacing Invariant Sections with translations requires special permission from their copyright holders, but you may include translations of some or all Invariant Sections in addition to the original versions of these Invariant Sections. You may include a translation of this License, and all the license notices in the Document, and any Warranty Disclaimers, provided that you also include the original English version of this License and the original versions of those notices and disclaimers. In case of a disagreement between the translation and the original version of this License or a notice or disclaimer, the original version will prevail.
If a section in the Document is Entitled "Acknowledgements", "Dedications", or "History", the requirement (section 4) to Preserve its Title (section 1) will typically require changing the actual title.
9. TERMINATION
You may not copy, modify, sublicense, or distribute the Document except as expressly provided for under this License. Any other attempt to copy, modify, sublicense or distribute the Document is void, and will automatically terminate your rights under this License. However, parties who have received copies, or rights, from you under this License will not have their licenses terminated so long as such parties remain in full compliance.
10. FUTURE REVISIONS OF THIS LICENSE
The Free Software Foundation may publish new, revised versions of the GNU Free Documentation License from time to time. Such new versions will be similar in spirit to the present version, but may differ in detail to address new problems or concerns. See http://www.gnu.org/copyleft/.
Each version of the License is given a distinguishing version number. If the Document specifies that a particular numbered version of this License "or any later version" applies to it, you have the option of following the terms and conditions either of that specified version or of any later version that has been published (not as a draft) by the Free Software Foundation. If the Document does not specify a version number of this License, you may choose any version ever published (not as a draft) by the Free Software Foundation.
New BSD Licence

Copyright (c) <YEAR>, <OWNER>
All rights reserved.

Redistribution and use in source and binary forms, with or without modification, are permitted provided that the following conditions are met:
* Redistributions of source code must retain the above copyright notice, this list of conditions and the following disclaimer.
* Redistributions in binary form must reproduce the above copyright notice, this list of conditions and the following disclaimer in the documentation and/or other materials provided with the distribution.
* Neither the name of the <ORGANIZATION> nor the names of its contributors may be used to endorse or promote products derived from this software without specific prior written permission.
THIS SOFTWARE IS PROVIDED BY THE COPYRIGHT HOLDERS AND CONTRIBUTORS "AS IS" AND ANY EXPRESS OR IMPLIED WARRANTIES, INCLUDING, BUT NOT LIMITED TO, THE IMPLIED WARRANTIES OF MERCHANTABILITY AND FITNESS FOR A PARTICULAR PURPOSE ARE DISCLAIMED. IN NO EVENT SHALL THE COPYRIGHT OWNER OR CONTRIBUTORS BE LIABLE FOR ANY DIRECT, INDIRECT, INCIDENTAL, SPECIAL, EXEMPLARY, OR CONSEQUENTIAL DAMAGES (INCLUDING, BUT NOT LIMITED TO, PROCUREMENT OF SUBSTITUTE GOODS OR SERVICES; LOSS OF USE, DATA, OR PROFITS; OR BUSINESS INTERRUPTION) HOWEVER CAUSED AND ON ANY THEORY OF LIABILITY, WHETHER IN CONTRACT, STRICT LIABILITY, OR TORT (INCLUDING NEGLIGENCE OR OTHERWISE) ARISING IN ANY WAY OUT OF THE USE OF THIS SOFTWARE, EVEN IF ADVISED OF THE POSSIBILITY OF SUCH DAMAGE.
Bibliography

[BOVET][RUBINI]